## Slide 1: TEMPERATURE FORECAST 3 HOURS AHEAD ON FPGA
Ngày 25 tháng 09 năm 2026
ĐỒ ÁN CE436.R11.VMTN
GVHD: Ts. Trần Xuân Phước
Thành viên:
  Nguyễn Nghĩa Khoa 24520832
  Nguyễn Minh Khoa 24520831
  Lê Đăng Khoa 24520816

## Slide 2: Project Scope: 3-Hour Forecast Core
ASSIGNED TOPIC: Weather Pattern Forecasting on FPGA using Time Series Analysis
ENGINEERING OBJECTIVES
Complete model-to-silicon design flow
C++ floating-point golden model
Bit-exact fixed-point Verilog RTL
Realistic edge DSP hardware practice
Focus: Hardware & DV mastery
Not claiming FPGA speedup on hourly data.
PROBLEM FORMULATION
Input: Hourly temperature T(t) (°C)
Output: Future temperature T̂(t+3) (°C)
Location: Single-station weather series
Source: NASA POWER hourly dataset
Target: 3-hour ahead local prediction
Tractable scope for a rigorous 3-month cycle.

## Slide 3: End-to-End System Workflow
1. OFFLINE TRAINING & GOLDEN MODEL (HOST C++)
Clean CSV Data → Least Squares Fit → Export Fixed-Point Model & Vectors
Solves weights a, b, c via Eigen C++ · Generates bit-exact test vectors for RTL
2. RUNTIME INFERENCE (TARGET FPGA CORE)
Sample T(t) In → [ 25-Sample Buffer + MAC Core ] → Forecast T̂(t+3) Out
Fixed coefficients on-chip · Valid handshake · Pipelined arithmetic datapath

## Slide 4: Linear Model with Diurnal Anchor & Taps
T̂(t+3) = T(t−21) + a[T(t) − T(t−24)] + b[T(t) − T(t−3)] + c
PHYSICAL MEANING OF TAPS
T(t−21): Diurnal Anchor
Same hour yesterday: (t+3) − 24 = t − 21
T(t) − T(t−24): Inter-Day Trend
Today vs. yesterday at current hour
T(t) − T(t−3): Recent Gradient
Latest 3-hour temperature rate of change
NUMERICAL WALKTHROUGH
Inputs: T(t−24)=19°, T(t−21)=21° T(t−3)=18°, T(t)=20°C
Weights: a = 0.5, b = 0.2, c = 0.0
21 + 0.5(1) + 0.2(2) = 21.9°C
Datapath: Subtract → Multiply → Adder Tree

## Slide 5: Chronological Training & Data Split
Regression Target: y = a·x₁ + b·x₂ + c
x₁ = T(t)−T(t−24) · x₂ = T(t)−T(t−3) · y = T(t+3)−T(t−21) Solved via C++ OLS
01 TRAIN
Past historical records
Fit weights a, b, c
Eigen least squares
02 VALIDATE
Model evaluation
Tune Q-format widths
Profile dynamic range
03 TEST
Unseen future period
Final accuracy score
Zero look-ahead leakage
Strict chronological order: Past history provides buffer context without label leakage.

## Slide 6
Algorithmic Baseline Benchmarking
EVALUATION METRIC: MAE
Mean Absolute Error on held-out test data:
MAE = (1/N) ∑ |T̂(i) − T_true(i)|
Core Evaluation Question:
Does our hardware model actually outperform simple no-math heuristics?
TWO NAIVE BASELINES
1. Persistence Baseline: T̂(t+3) = T(t)
Assumes temperature stays unchanged
2. Diurnal Baseline: T̂(t+3) = T(t−21)
Assumes today repeats yesterday at same hour
Academic Integrity Standard:
Residuals and MAE are reported honestly. Evaluated on identical test period.

## Slide 7: Fixed-Point Design & Q-Format
1. PROFILE RANGE
Sub-zero winter peaks
High summer extremes
Weight dynamic range
2. SELECT FORMAT
Signed fixed-point
Integer guard bits
E.g., Q8.8 or Q10.6
3. UNIFY RULES
Multiplier bit-growth
Truncation & shift logic
Saturation on overflow
GOLDEN VERIFICATION PRINCIPLE
C++ fixed-point golden model mirrors every RTL truncation & saturation step.
Separates forecast accuracy from quantization noise, guaranteeing 100% bit-exact RTL.

## Slide 8: Two-Phase Development Strategy
PHASE 1: CORE MVP (WEEKS 1–4)
PHASE 2: ADVANCED (WEEKS 5–8)
Goal: De-risk baseline silicon flow
Single-variable temperature core
25-stage shift register buffer
Bit-exact C++ fixed-point model
Synthesizable Verilog RTL & TB
Deliverable (Milestone 2):
Guaranteed working silicon baseline.
Goal: Depth for 3 students
Multi-variable (RH, P) expansion
Parallel vs. Shared-MAC trade-off
Advanced DV: Coverage & assertions
Physical FPGA board demo
Deliverable (Milestone 4):
Complete demo + trade-off report.

## Slide 9: Hardware Architecture & Datapath
25-SAMPLE BUFFER
Shift Reg: T(t−24)…T(t)
Required Hardware Taps:
t − 24 (Yesterday baseline)
t − 21 (Diurnal anchor)
t − 3 (Recent 3h change)
t (Current sample)
PIPELINED ARITHMETIC DATAPATH
Branch 1: [ T(t) − T(t−24) ] × a (Inter-day change)
Branch 2: [ T(t) − T(t−3) ] × b (3-hour rate of change)
Adder Tree: T(t−21) + Br₁ + Br₂ + c → T̂(t+3)
Saturation logic prevents arithmetic wrap-around on overflow
Forecast valid asserted only after 25 samples are buffered
Hardware latency: 2–4 clock cycles (nanoseconds) · Data step: 1 sample = 1 hour

## Slide 10: Demonstration via Accelerated Replay
HOST PC
Reads historical CSV
Streams T(t) samples
Retains T(t+3) label
Live Python UI
FPGA BOARD
UART RX module
25-stage shift register
Computes T̂(t+3)
UART TX Output
SCOREBOARD
Matches with T(t+3)
Calculates live MAE
Plots predicted vs true
Zero Leakage
Accelerated Replay: 1,000+ predictions demonstrated in under 2 minutes over UART.

## Slide 11: Three Verification Layers
01 / C++
FLOAT ↔ FIXED
Quantization SNR drop
Sub-zero temperatures
Dynamic range extremes
Validate Math & Q-format
02 / SIM
TB ↔ RTL CORE
100% bit-exact match
Reset & buffer warm-up
Pause & gap injection
Validate RTL Logic
03 / BOARD
FPGA ↔ REF.
Physical UART timing
Packet endianness
Scoreboard logging
Validate Hardware I/O

## Slide 12: Hardware Architecture Trade-Off Study
ARCH A: PARALLEL DSP
Dedicated Multipliers per Branch
Parallel units for Δday and Δ3h
Latency: 2 clock cycles
Throughput: 1 prediction / cycle
Resource: Uses multiple DSP slices
Target: High-speed multi-channel sensing
ARCH B: SHARED-MAC FSM
Time-Multiplexed Single MAC
Single shared multiplier-accumulator
FSM controller cycles through taps
Latency: 5–6 clock cycles
Resource: Ultra-compact (1 or 0 DSPs)
Target: Ultra-low-power IoT edge nodes
Evaluation: Synthesize both on target FPGA to compare LUTs, DSPs, and Fmax.

## Slide 13: 8-Week Execution Roadmap
Week | Phase | Tasks
Week 1–2 | Data & Base | • Clean NASA CSV • Set baselines • C++ float OLS
Week 3–4 | Phase 1 MVP | • Q-format profile • 25-stage RTL • Bit-exact TB
Week 5–6 | Phase 2 Scope | • Multi-var (RH, P) • Shared-MAC FSM • UART controller
Week 7–8 | Demo & Report | • Live UART demo • Coverage metrics • Synthesis report

## Slide 14: Three Students Workload Distribution
STUDENT 1
Algorithms & Data
Phase 1: Baseline Core
CSV cleaning & repair
Baselines & OLS solver
C++ golden model
Phase 2: Advanced
Multi-var (RH, P) data
Quantization SNR analysis
STUDENT 2
RTL & Architecture
Phase 1: Baseline Core
25-stage shift register
Pipelined datapath
Saturation logic
Phase 2: Advanced
Shared-MAC FSM design
FPGA synthesis study
STUDENT 3
DV & Demonstration
Phase 1: Baseline Core
Automated test vectors
Bit-exact RTL testbench
Warm-up & reset tests
Phase 2: Advanced
UART controller & demo
Code coverage metrics

## Slide 15: One Forecast, Two Claims to Verify
Phased Linear Model → Temperature +3 Hours
01 Forecast Quality
Prove model outperforms naive baselines on unseen future test data.
02 Hardware Correctness
Prove RTL matches the C++ fixed-point golden model bit-for-bit.