## Slide 1: TEMPERATURE FORECAST
3 HOURS AHEAD ON FPGA
A linear model from past values
CE436 / PROJECT PROPOSAL / SESSION 1
Past data
Now
+3 h
3 students · 12 weeks · C++ + Verilog/SystemVerilog
Notes: Good afternoon, professor and classmates. Our group proposes a three-hour-ahead temperature forecast on an FPGA using a linear model built from past values. This is a focused version of the assigned weather forecasting topic. Today we present the proposed method and twelve-week plan; we do not yet have fitted coefficients, accuracy results, or a board demonstration.

## Slide 2: A testable forecasting task
ASSIGNED TOPIC
Weather Pattern Forecasting on FPGA using Time Series Analysis
INPUT
Hourly temperature at one location, up to time t
OUTPUT
One temperature forecast at t + 3 h Unit: °C
Why a linear model?
Clear arithmetic; C++ and RTL can be compared within 3 months.
Core: one variable, fixed coefficients. Add humidity/pressure only if time allows. FPGA is for DSP/RTL practice; no speedup claim for hourly data.
Notes: We narrow the broad weather forecasting topic to hourly temperature at one location. At time t, the model uses observations available up to t and outputs a forecast for t plus three hours, in degrees Celsius. A linear model gives us clear arithmetic that we can reproduce in C++ and RTL within three months. FPGA speedup is not our claim for data that arrives only once an hour; our objective is the complete model-to-hardware workflow.

## Slide 3: C++ trains; FPGA forecasts
OFFLINE / PC
Temperature CSV
C++ training
Coefficients a, b, c
Clean → baselines → fit coefficients → fixed-point reference + test vectors
RUNTIME / COEFFICIENTS FIXED
Sample T(t)
FPGA
Forecast T̂(t+3)
Store history · compute · output
DELIVERABLES: C++ · RTL · testbench · board demo · error/resource report
Notes: The system has an offline stage and an FPGA runtime stage. C++ checks the CSV data, builds simple baselines, fits coefficients a, b, and c, and creates a fixed-point reference and test vectors. The FPGA receives temperature samples, stores the required history, and computes the forecast with coefficients fixed at runtime. Our deliverables are the C++ program, RTL, testbench, board demo, and an evaluation report.

## Slide 4: Four past values, one +3 h target
Planned source: NASA POWER • hourly T2M
Gridded data; location and date range TBD. Check missing/duplicate hours, time zone, and units.
t−24
t−21
t−3
t
t+3
t + 3 − 24 = t − 21
t−21 is the same hour on the day before the target.
Keep 25 consecutive samples. FPGA sees data through t; T(t+3) is for evaluation. Timeline shows order, not time intervals to scale.
Planned source: NASA POWER — hourly API documentation
Notes: We plan to use hourly NASA POWER T2M data, which is gridded data for a selected coordinate rather than a sensor reading at an exact point. We will confirm the coordinate, date range, time convention, units, and any missing or duplicate hours before creating samples. The value at t minus twenty-one hours is the same hour on the previous day relative to the target at t plus three hours. A buffer of twenty-five consecutive samples covers t minus twenty-four through t; the future target is used only as a training or evaluation label.

## Slide 5: A linear model from past values
T̂(t+3) = T(t−21) + a[T(t)−T(t−24)]
+ b[T(t)−T(t−3)] + c
T(t−21)
Same-hour anchor on the previous day
a[T(t)−T(t−24)]
Correction for day-to-day difference
b[T(t)−T(t−3)]
Correction for recent 3-hour change
c is a constant offset. C++ fits a, b, c offline; FPGA uses them unchanged. Proposed model only; no fitted coefficients or measured results yet.
Notes: The forecast starts from the temperature at the same hour on the previous day relative to the target. One correction uses the difference between the current hour and the same hour a day earlier; another uses the change over the latest three hours. C++ will estimate the two weights and constant offset from historical data, and the FPGA will use those fixed values. The model is a hypothesis that still needs comparison against baselines on unseen data.

## Slide 6: How is one forecast computed?
ILLUSTRATIVE EXAMPLE — values below are not measured results.
T(t−24)=19°C T(t−21)=21°C T(t−3)=18°C T(t)=20°C
Example coefficients: a = 0.5; b = 0.2; c = 0°C
21 + 0.5 × (20−19) + 0.2 × (20−18)
= 21 + 0.5 + 0.4
21.9°C
Hardware operations: subtract → multiply → add
Notes: This is an invented arithmetic example, not an experimental result. With past temperatures of nineteen, twenty-one, eighteen, and twenty degrees Celsius and example coefficients a equal to zero point five, b equal to zero point two, and c equal to zero, the forecast is twenty-one point nine degrees Celsius. The hardware therefore needs subtraction, multiplication by coefficients, and addition. A correct computation does not by itself establish forecast accuracy.

## Slide 7: Train on the past, test on the future
x₁ =
T(t)−T(t−24)
x₂ =
T(t)−T(t−3)
y =
T(t+3)−T(t−21)
y≈ax₁
+bx₂
+c
C++ fits a, b, c by least squares.
01 TRAIN
Fit coefficients on earlier data
02 VALIDATION
Select features and settings
03 TEST
Final evaluation on later data
Training labels cannot cross into validation/test; observed history remains usable. Split chronologically; ratios TBD. C++ may use Eigen for least squares.
Implementation reference: Eigen — Solving linear least squares systems
Notes: We rewrite the model as a small linear regression problem: x one is the day-to-day difference, x two is the recent three-hour difference, and y is the target temperature minus the same-hour anchor. C++ fits a, b, and c by least squares on training data. We divide data chronologically into training, validation, and test periods; training labels must not extend into later periods. Previously observed history may still be used as input when forecasting in a later period.

## Slide 8: Two evaluations, two questions
IS THE FORECAST USEFUL?
HARDWARE CORRECT?
Compare on the same test set:
Current value: T(t)
Same hour yesterday: T(t−21)
Proposed model
MAE (°C)
Mean absolute forecast error.
No results yet.
Float ↔ fixed
Measure quantization error.
RTL ↔ fixed reference
Bit-exact with valid and latency.
LUT / FF / DSP / latency
From synthesis results.
Error limits will be set after experiments.
Baseline reference: Forecasting: Principles and Practice — Simple forecasting methods
​
​
Notes: Our first question is whether the forecast improves on simple alternatives: the current temperature and the same-hour value from the previous day. We will compare all methods on the same test timestamps using mean absolute error in degrees Celsius. Our second question is whether the hardware follows its specification: we compare floating point with fixed point, then require RTL to match the fixed-point reference bit for bit at the correct valid cycle. LUT, flip-flop, DSP, and latency figures will come from synthesis rather than estimates.

## Slide 9: Fixed-point starts with value ranges
C++ FLOAT
Model's reference
ANALYZE BEFORE CHOOSING BITS
Temperature · coefficient · intermediate ranges
Q format TBD until data and coefficients are known.
C++ FIXED AND RTL FOLLOW ONE SPEC
Signedness · fractional bits · product and sum widths
Shifts · rounding · overflow: saturation or wrap
C++ reference mirrors each RTL arithmetic step.
Test negative temperatures, numeric limits, and overflow. Forecast error vs. truth and fixed-vs-float error are separate.
Notes: We will start with a floating-point C++ model and inspect the ranges of temperatures, fitted coefficients, products, and sums before choosing a fixed-point format. The specification must include signedness, fractional bits, intermediate widths, shifts, rounding, and overflow behavior. A C++ fixed-point reference will mirror the RTL operation by operation, including width reductions. Forecast error against measured temperature and fixed-point error against the floating-point model are different quantities.

## Slide 10: From sample history to arithmetic
Receive T(t)
25 SAMPLES
T(t−24)…T(t)
Required taps:
t−24, t−21
t−3, t
a × Δday
b × Δ3h
+
T(t−21), c
T̂(t+3)
Functional diagram; multiplier layout TBD.
Clock + valid accept samples. Forecast only after 25 valid samples. Coefficients stay fixed; choose shared or parallel multipliers after board selection. One sample delay = 1 data hour. Hardware latency is in clock cycles, not 3 hours.
Notes: The FPGA accepts a new sample only when valid is asserted. It stores twenty-five samples so it can read the four required time indices, forms two differences, multiplies them by the fixed coefficients, and adds the anchor and offset. The diagram describes functions, not a final choice between shared and parallel multipliers. A delay of one sample represents one hour in the data sequence, whereas hardware latency is measured in clock cycles; the circuit does not wait three real hours to forecast.

## Slide 11: Three verification layers
01 / C++
FLOAT ↔ FIXED
Measure error from quantization
Test: negative temps, limits, rapid changes.
02
TB ↔ RTL
Compare each output with valid and latency
Target: bit-exact. Test reset, overflow, warm-up, valid gaps.
03
BOARD ↔ REF.
Check interfaces and integrated output
Use the same vectors; check sample order, input and output logs.
Same data and arithmetic rules; each layer answers a different question.
​
​
​
Notes: We propose three layers of verification using the same input vectors. C++ compares floating-point and fixed-point calculations, especially at negative values and numeric limits. The testbench checks bit-exact RTL outputs at the expected valid cycle and covers reset, overflow, buffer warm-up, and gaps between accepted samples. The board run checks sample order, data encoding, interface behavior, and output logs against the reference.

## Slide 12: Demo by replaying historical data
Replay quickly while preserving time order.
Proposed demo; no board run or live interface yet.
PC / CSV
Send samples through t
UART if board permits
FPGA
Receive samples Compute T̂(t+3)
Return result to PC
PC / COMPARE
Compare results by hour
Log and display
PC holds T(t+3) for evaluation; future labels never enter FPGA. Board, interface, and minimum demo scope need instructor input.
Notes: The proposed demonstration replays historical data from a PC into the FPGA in chronological order, faster than real time. UART is one possible interface, depending on the available board. The PC logs the returned forecasts and compares each one with the target temperature in the CSV. At each forecast step, only samples through time t enter the FPGA; the future label remains on the PC for evaluation.

## Slide 13: 12 weeks, four milestones
WEEKS 1–3
Data
Learn basics Clean CSV Two baselines
WEEKS 4–6
C++ model
Fit + validate Select features Start fixed-point
WEEKS 7–9
RTL + testbench
Arithmetic core Bit comparison Prepare integration
WEEKS 10–12
Board + report
Demo + test Hardware resources Limits and conclusions
Each phase has a working deliverable; session 2 follows the instructor's schedule.
​
​
​
​
Notes: We divide twelve weeks into four stages with a working deliverable at each milestone. Weeks one to three cover foundations, clean data, and two baselines; weeks four to six cover C++ training, validation, and initial fixed-point analysis. Weeks seven to nine cover RTL and bit-exact testbench checks, while preparing board integration. The final three weeks cover the demo, held-out test evaluation, synthesis figures, and limitations.

## Slide 14: Three students, coordinated outputs
STUDENT 1
Data + C++
CSV · baselines Coefficients · MAE · reference
RISK: MISSING HOURS
Validate and repair hours before building samples.
STUDENT 2
Fixed-point + RTL
Buffer · arithmetic core Synthesis · board integration
RISK: BOARD TBD
Build a standalone core and simulate it first.
STUDENT 3
Verification + demo
Vectors · bit checking I/O · result logs
RISK: HIGH ERROR
Revisit validation together; report test results honestly.
Agree on data, coefficients, signedness, rounding/overflow, valid, and latency.
​
​
​
Notes: One student leads data and C++, another leads fixed-point RTL, and the third leads verification and the demonstration. The group must agree early on data formats, coefficient encoding, signed arithmetic, rounding, overflow, valid, and latency. Missing or misaligned hours are checked before sample creation; if the board is undecided, we can still complete and simulate a standalone core. If forecast error is high, we will analyze it on validation and report the held-out test result honestly.

## Slide 15: One forecast, two claims to verify
Linear model → temperature +3 h
01 Forecast quality
Compare with baselines on unseen data.
02 Hardware correctness
RTL matches the fixed-point reference.
Instructor input: +3 h scope · board/tools · minimum demo. Add humidity/pressure only after the core is complete.
​
Notes: Our proposed outcome is a three-hour-ahead temperature forecast from past hourly values, with coefficients trained in C++ and fixed-point inference on an FPGA. We will provide two kinds of evidence: forecast quality against baselines on unseen data, and RTL correctness against the fixed-point reference. We would welcome feedback on the three-hour scope, the FPGA board and tools, and the minimum expected board demonstration. Humidity or pressure would be added only after the core work is complete.