## Slide 1: TEMPERATURE FORECAST
3 HOURS AHEAD ON FPGA
A linear model from past values · Phased hardware architecture
CE436 / PROJECT PROPOSAL / SESSION 1
Past data
Now
+3 h
3 students · 12 weeks · Phase 1 MVP + Phase 2 Architecture Exploration
Notes: Good afternoon, Professor and classmates. Our group proposes a three-hour-ahead temperature forecasting system on FPGA using a linear time-series model built from past values. This is a focused, rigorous realization of the assigned weather forecasting topic. Today we present our proposed algorithmic model, hardware micro-architecture, and upgraded twelve-week execution plan.

## Slide 2: A testable forecasting task
ASSIGNED TOPIC
Weather Pattern Forecasting on FPGA using Time Series Analysis
INPUT
Hourly temperature at one location, up to time t
OUTPUT
One temperature forecast at t + 3 h Unit: °C
Why a linear time-series model?
Transparent arithmetic: allows exact bit-level cross-verification between C++ and RTL.
Phase 1 core: 1 variable, fixed coefficients. Phase 2 expands to humidity & pressure. FPGA is for DSP/RTL practice; no speedup claim for data arriving once an hour.
Notes: We deliberately narrow the broad weather forecasting topic down to hourly temperature at a specific geographic location. At hour t, the model ingests observations available up to t and outputs a forecast for t plus three hours in degrees Celsius. A linear model provides clear, auditable arithmetic that we can reproduce identically in C++ and RTL within three months. FPGA speedup is not our claim for data that arrives only once an hour; our real objective is mastering the complete model-to-hardware workflow.

## Slide 3: C++ trains; FPGA forecasts
OFFLINE / PC (TRAINING & SPECIFICATION)
Temperature CSV
C++ Training
Weights a, b, c
Clean CSV → compute baselines → least squares fit → fixed-point reference + test vectors
RUNTIME / FPGA (COEFFICIENTS FIXED ON-CHIP)
Sample T(t)
FPGA Core
Forecast T̂(t+3)
25-Sample Buffer · Arithmetic Pipeline · Valid Out
DELIVERABLES: C++ Suite · Synthesizable RTL · Bit-Exact Testbench · Board Demo · Report
Notes: The system separates offline algorithmic training from FPGA runtime inference. Offline in C++, we clean the NASA CSV dataset, establish baseline metrics, solve for model weights using least squares, and generate a bit-exact fixed-point golden reference alongside test vectors. The FPGA accepts sequential samples, buffers the history, and computes predictions with fixed coefficients on-chip. Our tangible deliverables include the C++ reference suite, synthesizable RTL, testbench, board demo, and comprehensive resource report.

## Slide 4: Linear model with diurnal anchor & taps
T̂(t+3) = T(t−21) + a[T(t) − T(t−24)] + b[T(t) − T(t−3)] + c
TAPS & PHYSICAL MEANING
T(t−21): Diurnal anchor Same hour yesterday: (t+3) − 24 = t − 21
T(t) − T(t−24): Inter-day trend Today vs. yesterday at current hour t
T(t) − T(t−3): Short-term gradient Recent 3-hour temperature rate of change
NUMERICAL ARITHMETIC EXAMPLE
Inputs: T(t−24)=19°C, T(t−21)=21°C T(t−3)=18°C, T(t)=20°C
Weights: a = 0.5, b = 0.2, c = 0.0°C
21 + 0.5×(1) + 0.2×(2) = 21.9°C
Hardware datapath: Subtract → Multiply → Adder Tree
Requires 25-sample buffer (t−24 to t). Future target T(t+3) strictly stays on host PC for scoring. NASA POWER hourly T2M data verified for gaps before buffering.
Planned source: NASA POWER — hourly API documentation
Notes: This slide consolidates our mathematical model, physical tap meanings, and arithmetic execution. Relative to our forecast target at t plus three hours, the sample at t minus twenty-one hours acts as the diurnal anchor—exactly the same hour yesterday. The difference T(t) minus T(t minus twenty-four) captures the day-to-day trend, while T(t) minus T(t minus three) tracks the recent three-hour temperature gradient. In our numerical walkthrough, past temperatures of nineteen, twenty-one, eighteen, and twenty degrees Celsius with weights zero-point-five and zero-point-two yield a forecast of twenty-one point nine degrees Celsius through subtraction, multiplication, and an adder tree. A twenty-five sample buffer stores samples t minus twenty-four through t, while the future target stays strictly on the host PC.

## Slide 5: Train on the past, test on the future
x₁ = T(t) − T(t−24)
x₂ = T(t) − T(t−3)
y = T(t+3) − T(t−21)
Target: y = a·x₁ + b·x₂ + c
Formulated as Ordinary Least Squares (OLS) solved offline via C++ (Eigen library).
01 TRAIN
Fit weights a, b, c on historical data
02 VALIDATION
Tune Q-format bitwidths & feature choices
03 TEST
Unseen future data for final reporting
Strict chronological split avoids look-ahead data leakage (no randomized k-fold). Past observations remain accessible across split boundaries as input buffer context.
Implementation reference: Eigen — Solving linear least squares systems
Notes: We formulate the model as an Ordinary Least Squares problem: x one is the day-to-day change, x two is the recent three-hour change, and target y is the offset from the diurnal anchor. C++ fits weights a, b, and constant c on historical training data using the Eigen library. To prevent look-ahead data leakage, we enforce a strict chronological split into training, validation, and held-out test periods. Previously observed history crosses split boundaries only as input buffer context, never as future labels.

## Slide 6: Algorithmic baseline benchmarking
IS THE FORECAST USEFUL?
Evaluation Metric: MAE (°C)
Mean Absolute Error across all test hours:
MAE = (1/N) ∑ |T̂(i) − T_true(i)|
Core Evaluation Question:
Does our hardware linear model actually outperform simple no-math heuristics?
TWO NAIVE BASELINES
Baseline 1: Persistence T(t)
Assumes temperature stays unchanged. Predicts: T̂(t+3) = T(t)
Baseline 2: Diurnal T(t−21)
Assumes today repeats yesterday. Predicts: T̂(t+3) = T(t−21)
Honest Scientific Standard:
If the linear model does not beat baselines, we analyze residuals and report honestly.
Baseline reference: Forecasting: Principles and Practice — Simple forecasting methods
Notes: To establish scientific value, we must answer whether our linear model outperforms simple, no-math heuristics. We evaluate all methods using Mean Absolute Error in degrees Celsius across identical test timestamps. We benchmark against two naive baselines: Persistence, which assumes the temperature remains unchanged from t, and Diurnal, which assumes today exactly repeats yesterday at the same hour. If our linear model does not outperform these baselines, we analyze the residuals and report the findings with full academic integrity.

## Slide 7: Fixed-point starts with value ranges
1. PROFILE RANGES
Profile dataset min/max:
Negative winter temps
High summer peaks
Dynamic range of weights
2. CHOOSE Q-FORMAT
Signed wordlength:
Integer guard bits
Fractional bits
E.g., Q8.8 or Q10.6
3. ARITHMETIC RULES
Unified C++ & RTL rules:
Multiplier bit-growth (32b)
Truncation shift position
Saturation vs. wrap-around
CRUCIAL VERIFICATION PRINCIPLE
C++ fixed-point reference mirrors every single RTL truncation & saturation step.
Separates forecast error vs. truth from fixed-point quantization noise vs. floating point. Enables 100% bit-exact RTL verification.
Notes: Fixed-point hardware implementation begins by profiling dynamic ranges across historical records: capturing sub-zero winter temperatures, peak summer heat, and coefficient magnitudes. We select an optimal signed Q-format, such as Q8.8 or Q10.6, balancing integer headroom against fractional precision. Our C++ fixed-point golden model mirrors every RTL truncation, shift, and saturation rule bit-for-bit. This separates statistical forecasting error against ground truth from quantization noise against floating point, enabling one hundred percent bit-exact RTL verification.

## Slide 8: Core MVP vs. Advanced extensions
PHASE 1: CORE MVP (WEEKS 1–6)
PHASE 2: EXTENSIONS (WEEKS 7–12)
Goal: De-risk the hardware flow
Single-variable temperature predictor
25-stage shift register history buffer
Bit-exact fixed-point C++ golden model
Synthesizable Verilog RTL & testbench
Deliverable Milestone 2:
Guaranteed working silicon baseline. Eliminates end-of-semester failure risk.
Goal: Engineering depth for 3 students
Multi-variable feature expansion: Add Relative Humidity (RH) & Pressure (P)
Hardware Trade-off Study: Parallel DSP vs. Shared-MAC FSM
Advanced DV: Code coverage & assertions
Deliverable Milestone 4:
Full FPGA board demo + architectural trade-off analysis justifying 3 students' effort.
​
​
Notes: To ensure project feasibility while demonstrating substantial engineering depth for three students, we divide our roadmap into two distinct phases. Phase one is our Core MVP, executed during Weeks one through six. It establishes a guaranteed working baseline: a single-variable temperature predictor, a twenty-five stage shift register buffer, and a synthesizable RTL core verified against C++. Phase two, running from Weeks seven to twelve, expands into advanced extensions: multi-variable features including relative humidity and pressure, an architectural trade-off study, and code-coverage verification. This two-phase strategy eliminates semester failure risk early.

## Slide 9: From sample history to arithmetic core
Receive T(t)
25 SAMPLES
T(t−24)…T(t)
Required taps:
t−24
t−21
t−3
t
a × Δday
b × Δ3h
+
T(t−21), c
T̂(t+3)
Pipelined datapath with saturation logic.
Clock + valid accept samples. Forecast asserted only after 25 valid samples (warm-up). Coefficients fixed on-chip; 1 sample step = 1 hourly interval in data sequence. Hardware latency is 2 to 4 clock cycles (nanoseconds), NOT 3 real hours!
Notes: Here we map the mathematical taps directly to the hardware datapath. A twenty-five stage shift register receives incoming samples when valid is asserted. Dedicated taps extract the four required indices, feeding two subtraction stages, two fixed-coefficient multipliers, and a pipelined adder tree with saturation logic. A delay of one sample represents one real-world hour in data, whereas hardware latency is only two to four clock cycles. The circuit produces a forecast in nanoseconds, never waiting three real hours.

## Slide 10: Demo by replaying historical data
HOST PC (PYTHON/C++)
Reads chronological CSV
Sends samples up to time t
Holds T(t+3) for scoring
Live Visual Dashboard
UART TX: T(t)
FPGA BOARD
UART RX module
25-stage shift register
Computes T̂(t+3)
UART TX module
UART RX: T̂(t+3)
SCOREBOARD & PLOT
Matches forecast with label
Calculates real-time MAE
Plots predicted vs. true curve
No Look-Ahead Leakage!
Accelerated Replay: Samples transmitted milliseconds apart instead of hours apart. Enables full demo of 1,000+ predictions in under 2 minutes during the final presentation. Future label T(t+3) never enters the FPGA; strictly preserved on host PC for verification.
Notes: Our hardware demonstration replays historical CSV records from a host PC to the FPGA in accelerated time. Samples are transmitted via UART milliseconds apart rather than hours apart, allowing us to demonstrate over one thousand sequential predictions in under two minutes. The FPGA processes each incoming sample, updates its buffer, and streams back the forecast. A host Python dashboard compares the prediction against the held-out target label and plots live error curves without any future data leakage.

## Slide 11: Three verification layers
01 / C++
FLOAT ↔ FIXED
Measure precision loss from quantization
Tests:
Negative temperatures
Max dynamic limits
Quantization SNR drop
02 / SIM
TB ↔ RTL CORE
Compare cycle-by-cycle with valid handshake
Target: 100% BIT-EXACT
Reset sequence
25-sample buffer warm-up
Pauses/gaps in valid_in
03 / BOARD
BOARD ↔ REF.
Check physical I/O & integrated system
Tests:
UART frame timing
Packet endianness
PC logging scoreboard
Same test vectors across all 3 tiers; each layer answers a distinct engineering question.
​
​
​
Notes: Verification proceeds across three hierarchical layers using identical test vectors. In Layer one, C++ compares floating-point against fixed-point arithmetic to measure quantization noise and test boundary conditions. In Layer two, the RTL simulation testbench verifies cycle-by-cycle valid handshakes, reset behavior, and buffer warm-up, requiring zero bit differences against the golden model. In Layer three, physical board tests validate UART timing, packet byte order, and end-to-end scoreboard synchronization.

## Slide 12: Hardware micro-architecture trade-off study
ARCH A: PARALLEL DSP
Dedicated Multipliers per Feature
Parallel multipliers for Δday and Δ3h
Latency: 2 clock cycles
Throughput: 1 prediction / clock cycle
Cost: Higher DSP slice / LUT count
Target Application:
High-speed sensor streams & multi-channel real-time thermal monitoring.
ARCH B: SHARED-MAC FSM
Time-Multiplexed Single Multiplier
1 shared multiplier-accumulator (MAC)
FSM controller cycles through tap inputs
Latency: N+2 cycles (e.g. 5–6 cycles)
Cost: Ultra-compact (1 DSP slice or 0 DSPs)
Target Application:
Ultra-low-power, area-constrained edge devices & battery-operated IoT weather stations.
Notes: As part of our Phase two engineering exploration, we conduct an architectural trade-off study comparing two distinct micro-architectures. Architecture A implements a fully parallel pipelined DSP datapath with dedicated multipliers for maximum throughput, targeting high-speed multi-channel sensing. Architecture B implements a resource-shared single-MAC architecture driven by a finite state machine, time-multiplexing multiplications into a single DSP slice or LUT-based multiplier. We will synthesize both architectures on our target FPGA and compare LUTs, DSP slices, and maximum operating frequency.

## Slide 13: 12 weeks, upgraded two-phase milestones
WEEKS 1–3
Data & Baseline
Clean NASA CSV
Persistence baseline
Diurnal baseline
C++ float OLS fit
WEEKS 4–6
Phase 1 MVP
Fixed-point profile
25-stage RTL core
Bit-exact TB match
Initial Vivado synth
WEEKS 7–9
Phase 2 Scope
Multi-var (T+RH+P)
Shared-MAC FSM
Arch trade-off study
UART controller RTL
WEEKS 10–12
Demo & Defense
Live UART PC demo
DV code coverage
LUT/FF/DSP report
Final report writing
Phase 1 secures a working baseline by Week 6; Phase 2 explores hardware & feature depth.
​
​
​
​
Notes: Our upgraded twelve-week schedule establishes four concrete milestones, each yielding a working deliverable. Weeks one to three deliver clean NASA data, baselines, and C++ floating-point training. Weeks four to six complete the Phase one Core MVP with a synthesizable RTL core and bit-exact simulation. Weeks seven to nine advance Phase two with multi-variable modeling, the shared-MAC architecture, and UART controller integration. Weeks ten to twelve finalize the live hardware demonstration, code coverage, synthesis resource analysis, and defense report.

## Slide 14: Three students, two-phase workload
STUDENT 1
Algorithms & Data
Phase 1: Baseline Core
CSV cleaning & gap repair
Baseline models & OLS fit
C++ fixed-point golden model
Phase 2: Advanced Scope
Multi-variable data (RH, P)
ARX / non-linear models
Quantization SNR analysis
STUDENT 2
RTL & Architecture
Phase 1: Baseline Core
25-stage shift register RTL
Fixed-point pipelined datapath
Saturation & valid handshake
Phase 2: Advanced Scope
Parallel vs. Shared-MAC FSM
Area & Fmax optimization
Synthesis on target FPGA
STUDENT 3
DV & System Demo
Phase 1: Baseline Core
Automated test vector suite
Bit-exact RTL testbench
Reset & warm-up verification
Phase 2: Advanced Scope
UART controller integration
PC live display dashboard
Code coverage & assertions
Unified arithmetic specification co-authored early: wordlengths, rounding, saturation, valid, latency.
​
​
​
Notes: The workload is evenly distributed across three students across both project phases. Student One leads algorithms and data, delivering the C++ golden model in Phase one and multi-variable modeling in Phase two. Student Two leads RTL design, building the pipelined datapath in Phase one and conducting the architectural trade-off study in Phase two. Student Three leads verification and demo, constructing the bit-exact testbench in Phase one and integrating the UART controller and live PC dashboard in Phase two. All interfaces and arithmetic conventions are agreed upon at kickoff.

## Slide 15: One forecast, two claims to verify
Phased Linear Model → Temperature +3 h
01 Forecast quality
Compare with Persistence and Diurnal baselines on unseen data.
02 Hardware correctness
RTL matches the C++ fixed-point golden reference bit-for-bit.
Instructor input: 1. Confirm scope (Phase 1 MVP → Phase 2) · 2. Board/tools · 3. Demo expectation. Multi-variable expansion & architecture exploration follow the baseline core.
​
Notes: In summary, our project delivers a three-hour-ahead temperature forecasting system on FPGA, rigorously backed by two distinct proofs: proving forecasting quality against naive baselines on unseen data, and proving hardware correctness bit-for-bit against a golden fixed-point model. Before we proceed, we welcome the professor's feedback on our three-hour prediction scope, recommended FPGA board and toolchain, and minimum demo expectations. Thank you for your time, and we look forward to your guidance.