## Slide 1: 3-Hour Temperature Forecast on FPGA
Linear Time-Series Modeling & RTL Verification
CE436 DSP Project Proposal · 12-Week Roadmap · 3 Members
Notes: Good afternoon, Professor and classmates. Our group proposes a three-hour-ahead temperature forecasting system on FPGA using a linear time-series model built from past values. This is a focused, rigorous realization of the assigned weather forecasting topic. Today we present our proposed algorithmic model, hardware micro-architecture, and upgraded twelve-week execution plan.

## Slide 2: Project Scope: 3-Hour Forecast Core
PROBLEM FORMULATION
Input: Hourly temperature T(t) (°C)
Output: Future temperature T̂(t+3) (°C)
Location: Single-station weather series
Source: NASA POWER hourly dataset
Target: 3-hour ahead local prediction
Tractable scope for a rigorous 3-month cycle.
ENGINEERING OBJECTIVES
Complete model-to-silicon design flow
C++ floating-point golden model
Bit-exact fixed-point Verilog RTL
Realistic edge DSP hardware practice
Focus: Hardware & DV mastery
Not claiming FPGA speedup on hourly data.
Single-variable core de-risks execution; multi-variable inputs are Phase 2 extensions.
Notes: We deliberately narrow the broad weather forecasting topic down to hourly temperature at a specific geographic location. At hour t, the model ingests observations available up to t and outputs a forecast for t plus three hours in degrees Celsius. A linear model provides clear, auditable arithmetic that we can reproduce identically in C++ and RTL within three months. FPGA speedup is not our claim for data that arrives only once an hour; our real objective is mastering the complete model-to-hardware workflow.

## Slide 3: End-to-End System Workflow
1. OFFLINE TRAINING & GOLDEN MODEL (HOST C++)
Clean CSV Data → Least Squares Fit → Export Fixed-Point Model & Vectors
Solves weights a, b, c via Eigen C++ · Generates bit-exact test vectors for RTL
2. RUNTIME INFERENCE (TARGET FPGA CORE)
Sample T(t) In → [ 25-Sample Buffer + MAC Core ] → Forecast T̂(t+3) Out
Fixed coefficients on-chip · Valid handshake · Pipelined arithmetic datapath
DELIVERABLES: C++ Suite · Synthesizable RTL · Bit-Exact TB · Board Demo · Report
Notes: The system separates offline algorithmic training from FPGA runtime inference. Offline in C++, we clean the NASA CSV dataset, establish baseline metrics, solve for model weights using least squares, and generate a bit-exact fixed-point golden reference alongside test vectors. The FPGA accepts sequential samples, buffers the history, and computes predictions with fixed coefficients on-chip. Our tangible deliverables include the C++ reference suite, synthesizable RTL, testbench, board demo, and comprehensive resource report.

## Slide 4: Linear Model with Diurnal Anchor & Taps
T̂(t+3) = T(t−21) + a[T(t) − T(t−24)] + b[T(t) − T(t−3)] + c
PHYSICAL MEANING OF TAPS
T(t−21): Diurnal Anchor
Same hour yesterday: (t+3) − 24 = t − 21
T(t) − T(t−24): Inter-Day Trend
Today vs. yesterday at current hour
T(t) − T(t−3): Recent Gradient
Latest 3-hour temperature rate of change
NUMERICAL WALKTHROUGH
Inputs: T(t−24)=19°, T(t−21)=21° T(t−3)=18°, T(t)=20°C
Weights: a = 0.5, b = 0.2, c = 0.0
21 + 0.5(1) + 0.2(2) = 21.9°C
Datapath: Subtract → Multiply → Adder Tree
Planned source: NASA POWER — hourly API documentation
Notes: This slide consolidates our mathematical model, physical tap meanings, and arithmetic execution. Relative to our forecast target at t plus three hours, the sample at t minus twenty-one hours acts as the diurnal anchor—exactly the same hour yesterday. The difference T(t) minus T(t minus twenty-four) captures the day-to-day trend, while T(t) minus T(t minus three) tracks the recent three-hour temperature gradient. In our numerical walkthrough, past temperatures of nineteen, twenty-one, eighteen, and twenty degrees Celsius with weights zero-point-five and zero-point-two yield a forecast of twenty-one point nine degrees Celsius through subtraction, multiplication, and an adder tree. A twenty-five sample buffer stores samples t minus twenty-four through t, while the future target stays strictly on the host PC.

## Slide 5: Chronological Training & Data Split
Regression Target: y = a·x₁ + b·x₂ + c
x₁ = T(t)−T(t−24) · x₂ = T(t)−T(t−3) · y = T(t+3)−T(t−21) · Solved via C++ OLS
01 TRAIN
Past historical records
Fit weights a, b, c
Eigen least squares
02 VALIDATE
Model evaluation
Tune Q-format widths
Profile dynamic range
03 TEST
Unseen future period
Final accuracy score
Zero look-ahead leakage
Strict chronological order: Past history provides buffer context without label leakage.
Implementation reference: Eigen — Solving linear least squares systems
Notes: We formulate the model as an Ordinary Least Squares problem: x one is the day-to-day change, x two is the recent three-hour change, and target y is the offset from the diurnal anchor. C++ fits weights a, b, and constant c on historical training data using the Eigen library. To prevent look-ahead data leakage, we enforce a strict chronological split into training, validation, and held-out test periods. Previously observed history crosses split boundaries only as input buffer context, never as future labels.

## Slide 6: Algorithmic Baseline Benchmarking
EVALUATION METRIC: MAE
Mean Absolute Error on held-out test data:
MAE = (1/N) ∑ |T̂(i) − T_true(i)|
Core Evaluation Question:
Does our hardware model actually outperform simple no-math heuristics?
TWO NAIVE BASELINES
1. Persistence Baseline: T̂(t+3) = T(t)
Assumes temperature stays unchanged
2. Diurnal Baseline: T̂(t+3) = T(t−21)
Assumes today repeats yesterday at same hour
Academic Integrity Standard:
Residuals and MAE are reported honestly. Evaluated on identical test period.
Baseline reference: Forecasting: Principles and Practice — Simple forecasting methods
Notes: To establish scientific value, we must answer whether our linear model outperforms simple, no-math heuristics. We evaluate all methods using Mean Absolute Error in degrees Celsius across identical test timestamps. We benchmark against two naive baselines: Persistence, which assumes the temperature remains unchanged from t, and Diurnal, which assumes today exactly repeats yesterday at the same hour. If our linear model does not outperform these baselines, we analyze the residuals and report the findings with full academic integrity.

## Slide 7: Fixed-Point Design & Q-Format
1. PROFILE RANGE
Sub-zero winter peaks
High summer extremes
Weight dynamic range
2. SELECT FORMAT
Signed fixed-point
Integer guard bits
E.g., Q8.8 or Q10.6
3. UNIFY RULES
Multiplier bit-growth
Truncation & shift logic
Saturation on overflow
GOLDEN VERIFICATION PRINCIPLE
C++ fixed-point golden model mirrors every RTL truncation & saturation step.
Separates forecast accuracy from quantization noise, guaranteeing 100% bit-exact RTL.
Notes: Fixed-point hardware implementation begins by profiling dynamic ranges across historical records: capturing sub-zero winter temperatures, peak summer heat, and coefficient magnitudes. We select an optimal signed Q-format, such as Q8.8 or Q10.6, balancing integer headroom against fractional precision. Our C++ fixed-point golden model mirrors every RTL truncation, shift, and saturation rule bit-for-bit. This separates statistical forecasting error against ground truth from quantization noise against floating point, enabling one hundred percent bit-exact RTL verification.

## Slide 8: Two-Phase Development Strategy
PHASE 1: CORE MVP (WEEKS 1–6)
PHASE 2: ADVANCED (WEEKS 7–12)
Goal: De-risk baseline silicon flow
Single-variable temperature core
25-stage shift register buffer
Bit-exact C++ fixed-point model
Synthesizable Verilog RTL & TB
Deliverable (Milestone 2):
Guaranteed working silicon baseline.
Goal: Depth for 3 students
Multi-variable (RH, P) expansion
Parallel vs. Shared-MAC trade-off
Advanced DV: Coverage & assertions
Physical FPGA board demo
Deliverable (Milestone 4):
Complete demo + trade-off report.
​
​
Notes: To ensure project feasibility while demonstrating substantial engineering depth for three students, we divide our roadmap into two distinct phases. Phase one is our Core MVP, executed during Weeks one through six. It establishes a guaranteed working baseline: a single-variable temperature predictor, a twenty-five stage shift register buffer, and a synthesizable RTL core verified against C++. Phase two, running from Weeks seven to twelve, expands into advanced extensions: multi-variable features including relative humidity and pressure, an architectural trade-off study, and code-coverage verification. This two-phase strategy eliminates semester failure risk early.

## Slide 9: Hardware Architecture & Datapath
25-SAMPLE BUFFER
Shift Reg: T(t−24)…T(t)
Required Hardware Taps:
t − 24 (Yesterday baseline)
t − 21 (Diurnal anchor)
t − 3 (Recent 3h change)
t (Current sample)
PIPELINED ARITHMETIC DATAPATH
Branch 1: [ T(t) − T(t−24) ] × a (Inter-day change)
Branch 2: [ T(t) − T(t−3) ] × b (3-hour rate of change)
Adder Tree: T(t−21) + Br₁ + Br₂ + c → T̂(t+3)
Saturation logic prevents arithmetic wrap-around on overflow
Forecast valid asserted only after 25 samples are buffered
Hardware latency: 2–4 clock cycles (nanoseconds) · Data step: 1 sample = 1 hour
Notes: Here we map the mathematical taps directly to the hardware datapath. A twenty-five stage shift register receives incoming samples when valid is asserted. Dedicated taps extract the four required indices, feeding two subtraction stages, two fixed-coefficient multipliers, and a pipelined adder tree with saturation logic. A delay of one sample represents one real-world hour in data, whereas hardware latency is only two to four clock cycles. The circuit produces a forecast in nanoseconds, never waiting three real hours.

## Slide 10: Demonstration via Accelerated Replay
HOST PC
Reads historical CSV
Streams T(t) samples
Retains T(t+3) label
Live Python UI
FPGA BOARD
UART RX module
25-stage shift register
Computes T̂(t+3)
UART TX Output
SCOREBOARD
Matches with T(t+3)
Calculates live MAE
Plots predicted vs true
Zero Leakage
Accelerated Replay: 1,000+ predictions demonstrated in under 2 minutes over UART.
Notes: Our hardware demonstration replays historical CSV records from a host PC to the FPGA in accelerated time. Samples are transmitted via UART milliseconds apart rather than hours apart, allowing us to demonstrate over one thousand sequential predictions in under two minutes. The FPGA processes each incoming sample, updates its buffer, and streams back the forecast. A host Python dashboard compares the prediction against the held-out target label and plots live error curves without any future data leakage.

## Slide 11: Three Verification Layers
01 / C++
FLOAT ↔ FIXED
Quantization SNR drop
Sub-zero temperatures
Dynamic range extremes
Validate Math & Q-format
02 / SIM
TB ↔ RTL CORE
100% bit-exact match
Reset & buffer warm-up
Pause & gap injection
Validate RTL Logic
03 / BOARD
FPGA ↔ REF.
Physical UART timing
Packet endianness
Scoreboard logging
Validate Hardware I/O
Shared test vectors across all 3 tiers; each layer answers a distinct engineering question.
​
​
​
Notes: Verification proceeds across three hierarchical layers using identical test vectors. In Layer one, C++ compares floating-point against fixed-point arithmetic to measure quantization noise and test boundary conditions. In Layer two, the RTL simulation testbench verifies cycle-by-cycle valid handshakes, reset behavior, and buffer warm-up, requiring zero bit differences against the golden model. In Layer three, physical board tests validate UART timing, packet byte order, and end-to-end scoreboard synchronization.

## Slide 12: Hardware Architecture Trade-Off Study
ARCH A: PARALLEL DSP
Dedicated Multipliers per Branch
Parallel units for Δday and Δ3h
Latency: 2 clock cycles
Throughput: 1 prediction / cycle
Resource: Uses multiple DSP slices
Target: High-speed multi-channel sensing
ARCH B: SHARED-MAC FSM
Time-Multiplexed Single MAC
Single shared multiplier-accumulator
FSM controller cycles through taps
Latency: 5–6 clock cycles
Resource: Ultra-compact (1 or 0 DSPs)
Target: Ultra-low-power IoT edge nodes
Evaluation: Synthesize both on target FPGA to compare LUTs, DSPs, and Fmax.
Notes: As part of our Phase two engineering exploration, we conduct an architectural trade-off study comparing two distinct micro-architectures. Architecture A implements a fully parallel pipelined DSP datapath with dedicated multipliers for maximum throughput, targeting high-speed multi-channel sensing. Architecture B implements a resource-shared single-MAC architecture driven by a finite state machine, time-multiplexing multiplications into a single DSP slice or LUT-based multiplier. We will synthesize both architectures on our target FPGA and compare LUTs, DSP slices, and maximum operating frequency.

## Slide 13: 12-Week Execution Roadmap
WEEKS 1–3
Data & Base
Clean NASA CSV
Baselines
C++ float OLS
WEEKS 4–6
Phase 1 MVP
Q-format profile
25-stage RTL
Bit-exact TB
WEEKS 7–9
Phase 2 Scope
Multi-var (RH, P)
Shared-MAC FSM
UART controller
WEEKS 10–12
Demo & Report
Live UART demo
Coverage metrics
Synthesis report
Phase 1 secures working baseline by Week 6; Phase 2 delivers engineering depth.
​
​
​
​
Notes: Our upgraded twelve-week schedule establishes four concrete milestones, each yielding a working deliverable. Weeks one to three deliver clean NASA data, baselines, and C++ floating-point training. Weeks four to six complete the Phase one Core MVP with a synthesizable RTL core and bit-exact simulation. Weeks seven to nine advance Phase two with multi-variable modeling, the shared-MAC architecture, and UART controller integration. Weeks ten to twelve finalize the live hardware demonstration, code coverage, synthesis resource analysis, and defense report.

## Slide 14: Three Students Workload Distribution
STUDENT 1
Algorithms & Data
Phase 1: Baseline Core
CSV cleaning & repair
Baselines & OLS solver
C++ golden model
Phase 2: Advanced
Multi-var (RH, P) data
Quantization SNR analysis
STUDENT 2
RTL & Architecture
Phase 1: Baseline Core
25-stage shift register
Pipelined datapath
Saturation logic
Phase 2: Advanced
Shared-MAC FSM design
FPGA synthesis study
STUDENT 3
DV & Demonstration
Phase 1: Baseline Core
Automated test vectors
Bit-exact RTL testbench
Warm-up & reset tests
Phase 2: Advanced
UART controller & demo
Code coverage metrics
Shared arithmetic contract agreed at kickoff: wordlengths, rounding, saturation, valid, latency.
​
​
​
Notes: The workload is evenly distributed across three students across both project phases. Student One leads algorithms and data, delivering the C++ golden model in Phase one and multi-variable modeling in Phase two. Student Two leads RTL design, building the pipelined datapath in Phase one and conducting the architectural trade-off study in Phase two. Student Three leads verification and demo, constructing the bit-exact testbench in Phase one and integrating the UART controller and live PC dashboard in Phase two. All interfaces and arithmetic conventions are agreed upon at kickoff.

## Slide 15: One Forecast, Two Claims to Verify
Phased Linear Model → Temperature +3 Hours
01 Forecast Quality
Prove model outperforms naive baselines on unseen future test data.
02 Hardware Correctness
Prove RTL matches the C++ fixed-point golden model bit-for-bit.
Instructor feedback: 1. Confirm scope (Phase 1 MVP → Phase 2) · 2. Board/tools · 3. Demo expectation. Multi-variable expansion & architecture exploration follow the baseline core.
​
Notes: In summary, our project delivers a three-hour-ahead temperature forecasting system on FPGA, rigorously backed by two distinct proofs: proving forecasting quality against naive baselines on unseen data, and proving hardware correctness bit-for-bit against a golden fixed-point model. Before we proceed, we welcome the professor's feedback on our three-hour prediction scope, recommended FPGA board and toolchain, and minimum demo expectations. Thank you for your time, and we look forward to your guidance.