## Slide 1
01 / 15
CE436 / PROJECT PROPOSAL
TEMPERATURE
FORECAST ON FPGA
+3 h
from past hourly values
past
now
forecast
3 students • 12 weeks • C++ + Verilog/SystemVerilog
Notes: Good afternoon, Professor and classmates. Our group proposes a three-hour-ahead temperature forecasting system on FPGA using a linear time-series model built from past values. This is a focused, rigorous realization of the assigned weather forecasting topic. Today we present our proposed algorithmic model, hardware micro-architecture, and upgraded twelve-week execution plan.

## Slide 2
A testable forecasting task
02 / 15
INPUT
OUTPUT
Hourly temperature at one location
One temperature 3 hours ahead
Known through t
Forecast for t + 3 h
Notes: We deliberately narrow the broad weather forecasting topic down to hourly temperature at a specific geographic location. At hour t, the model ingests observations available up to t and outputs a forecast for t plus three hours in degrees Celsius. A linear model provides clear, auditable arithmetic that we can reproduce identically in C++ and RTL within three months. FPGA speedup is not our claim for data that arrives only once an hour; our real objective is mastering the complete model-to-hardware workflow.

## Slide 3
C++ trains. FPGA forecasts.
03 / 15
OFFLINE ON PC
Temperature CSV
C++ fitting
a, b, c
RUNTIME ON FPGA
New sample
FPGA core
T̂(t+3)
The coefficients stay fixed while the FPGA runs.
Notes: The system separates offline algorithmic training from FPGA runtime inference. Offline in C++, we clean the NASA CSV dataset, establish baseline metrics, solve for model weights using least squares, and generate a bit-exact fixed-point golden reference alongside test vectors. The FPGA accepts sequential samples, buffers the history, and computes predictions with fixed coefficients on-chip. Our tangible deliverables include the C++ reference suite, synthesizable RTL, testbench, board demo, and comprehensive resource report.

## Slide 4
Four past values. One future target.
04 / 15
t−24
t−21
t−3
t
t+3
t + 3 − 24 = t − 21
25 consecutive samples are stored; the future target is never an input.
Notes: This slide consolidates our mathematical model, physical tap meanings, and arithmetic execution. Relative to our forecast target at t plus three hours, the sample at t minus twenty-one hours acts as the diurnal anchor—exactly the same hour yesterday. The difference T(t) minus T(t minus twenty-four) captures the day-to-day trend, while T(t) minus T(t minus three) tracks the recent three-hour temperature gradient. In our numerical walkthrough, past temperatures of nineteen, twenty-one, eighteen, and twenty degrees Celsius with weights zero-point-five and zero-point-two yield a forecast of twenty-one point nine degrees Celsius through subtraction, multiplication, and an adder tree. A twenty-five sample buffer stores samples t minus twenty-four through t, while the future target stays strictly on the host PC.

## Slide 5
A linear model from past values
05 / 15
T̂(t+3) = T(t−21)
+ a[T(t)−T(t−24)]
+ b[T(t)−T(t−3)]
+ c
ANCHOR
same hour yesterday
DAY-TO-DAY
current vs. yesterday
RECENT CHANGE
latest 3 hours
Notes: We formulate the model as an Ordinary Least Squares problem: x one is the day-to-day change, x two is the recent three-hour change, and target y is the offset from the diurnal anchor. C++ fits weights a, b, and constant c on historical training data using the Eigen library. To prevent look-ahead data leakage, we enforce a strict chronological split into training, validation, and held-out test periods. Previously observed history crosses split boundaries only as input buffer context, never as future labels.

## Slide 6
How is one forecast computed?
06 / 15
ILLUSTRATIVE VALUES — NOT A MEASURED RESULT
19°C
t−24
21°C
t−21
18°C
t−3
20°C
t
a = 0.5 b = 0.2
21.0
anchor
+0.5
day shift
+0.4
3 h trend
21.9°C
subtract → multiply → add
Notes: To establish scientific value, we must answer whether our linear model outperforms simple, no-math heuristics. We evaluate all methods using Mean Absolute Error in degrees Celsius across identical test timestamps. We benchmark against two naive baselines: Persistence, which assumes the temperature remains unchanged from t, and Diurnal, which assumes today exactly repeats yesterday at the same hour. If our linear model does not outperform these baselines, we analyze the residuals and report the findings with full academic integrity.

## Slide 7
Train on the past. Test on the future.
07 / 15
x1 = T(t) − T(t−24)
x2 = T(t) − T(t−3)
y = a·x1 + b·x2 + c
fit a, b, c by least squares
01 TRAIN
fit coefficients
02 VALIDATE
select settings
03 TEST
evaluate once
Split chronologically; training labels must not cross into later periods.
Notes: Fixed-point hardware implementation begins by profiling dynamic ranges across historical records: capturing sub-zero winter temperatures, peak summer heat, and coefficient magnitudes. We select an optimal signed Q-format, such as Q8.8 or Q10.6, balancing integer headroom against fractional precision. Our C++ fixed-point golden model mirrors every RTL truncation, shift, and saturation rule bit-for-bit. This separates statistical forecasting error against ground truth from quantization noise against floating point, enabling one hundred percent bit-exact RTL verification.

## Slide 8
Does the model beat simple forecasts?
08 / 15
CURRENT VALUE
T(t)
SAME HOUR YESTERDAY
T(t−21)
LINEAR MODEL
T̂(t+3)
Compare MAE on the same held-out test timestamps.
Notes: To ensure project feasibility while demonstrating substantial engineering depth for three students, we divide our roadmap into two distinct phases. Phase one is our Core MVP, executed during Weeks one through six. It establishes a guaranteed working baseline: a single-variable temperature predictor, a twenty-five stage shift register buffer, and a synthesizable RTL core verified against C++. Phase two, running from Weeks seven to twelve, expands into advanced extensions: multi-variable features including relative humidity and pressure, an architectural trade-off study, and code-coverage verification. This two-phase strategy eliminates semester failure risk early.

## Slide 9
Fixed-point needs an explicit contract
09 / 15
C++ FLOAT
C++ FIXED
RTL
Define the arithmetic before coding RTL:
signedness
bit widths
rounding
overflow
Forecast error and quantization error are different measurements.
Notes: Here we map the mathematical taps directly to the hardware datapath. A twenty-five stage shift register receives incoming samples when valid is asserted. Dedicated taps extract the four required indices, feeding two subtraction stages, two fixed-coefficient multipliers, and a pipelined adder tree with saturation logic. A delay of one sample represents one real-world hour in data, whereas hardware latency is only two to four clock cycles. The circuit produces a forecast in nanoseconds, never waiting three real hours.

## Slide 10
From sample history to arithmetic
10 / 15
25-SAMPLE
BUFFER
t−24
t−21
t−3
t
day-to-day Δ
× a
recent 3 h Δ
× b
+
T̂(t+3)
Accept a sample on valid; output only after the buffer is ready.
Notes: Our hardware demonstration replays historical CSV records from a host PC to the FPGA in accelerated time. Samples are transmitted via UART milliseconds apart rather than hours apart, allowing us to demonstrate over one thousand sequential predictions in under two minutes. The FPGA processes each incoming sample, updates its buffer, and streams back the forecast. A host Python dashboard compares the prediction against the held-out target label and plots live error curves without any future data leakage.

## Slide 11
Three verification layers
11 / 15
01
C++
float vs. fixed
quantization
02
TESTBENCH
RTL vs. reference
bit-exact output
03
BOARD
integrated run
I/O and sample order
All layers use the same input vectors and arithmetic specification.
Notes: Verification proceeds across three hierarchical layers using identical test vectors. In Layer one, C++ compares floating-point against fixed-point arithmetic to measure quantization noise and test boundary conditions. In Layer two, the RTL simulation testbench verifies cycle-by-cycle valid handshakes, reset behavior, and buffer warm-up, requiring zero bit differences against the golden model. In Layer three, physical board tests validate UART timing, packet byte order, and end-to-end scoreboard synchronization.

## Slide 12
Replay historical data for the demo
12 / 15
PC / CSV
send past samples
FPGA
compute forecast
PC / CHECK
compare with truth
Only samples through t enter the FPGA.
Notes: As part of our Phase two engineering exploration, we conduct an architectural trade-off study comparing two distinct micro-architectures. Architecture A implements a fully parallel pipelined DSP datapath with dedicated multipliers for maximum throughput, targeting high-speed multi-channel sensing. Architecture B implements a resource-shared single-MAC architecture driven by a finite state machine, time-multiplexing multiplications into a single DSP slice or LUT-based multiplier. We will synthesize both architectures on our target FPGA and compare LUTs, DSP slices, and maximum operating frequency.

## Slide 13
12 weeks. Prototype early. Evaluate deeply.
13 / 15
W1–3
PROTOTYPE
data + C++ working RTL core
W4–6
VALIDATE
model vs. baselines fixed-point sweep
W7–9
HARDEN
bit-exact tests resource trade-offs
W10–12
DEMO
board integration final test + report
Each phase ends with a measurable deliverable.
Notes: We plan to build a working C++ and RTL prototype by the end of week three, including clean data and a basic end-to-end test. Weeks four through six focus on model validation and fixed-point precision experiments. Weeks seven through nine harden the RTL verification and compare hardware resource trade-offs. The final three weeks cover board integration, held-out test evaluation, and the report; the schedule is a proposal rather than a claim of completed work.

## Slide 14
Three students. Clear ownership.
14 / 15
STUDENT 1
DATA + C++
dataset + MAE coefficients
missing hours
STUDENT 2
FIXED + RTL
RTL core synthesis
board TBD
STUDENT 3
VERIFY + DEMO
test vectors interface + logs
high error
One shared contract: data, coefficients, rounding, valid, and latency.
Notes: The workload is evenly distributed across three students across both project phases. Student One leads algorithms and data, delivering the C++ golden model in Phase one and multi-variable modeling in Phase two. Student Two leads RTL design, building the pipelined datapath in Phase one and conducting the architectural trade-off study in Phase two. Student Three leads verification and demo, constructing the bit-exact testbench in Phase one and integrating the UART controller and live PC dashboard in Phase two. All interfaces and arithmetic conventions are agreed upon at kickoff.

## Slide 15
One forecast. Two things to prove.
15 / 15
01 FORECAST
QUALITY
Beat the baselines on unseen data
02 HARDWARE
CORRECTNESS
Match the C++ fixed- point reference
Feedback needed:
scope • FPGA board/tools • minimum demo
Notes: In summary, our project delivers a three-hour-ahead temperature forecasting system on FPGA, rigorously backed by two distinct proofs: proving forecasting quality against naive baselines on unseen data, and proving hardware correctness bit-for-bit against a golden fixed-point model. Before we proceed, we welcome the professor's feedback on our three-hour prediction scope, recommended FPGA board and toolchain, and minimum demo expectations. Thank you for your time, and we look forward to your guidance.