## Slide 1: TEMPERATURE FORECAST 3 HOURS AHEAD ON FPGA
Ngày 09 tháng 10 năm 2026
ĐỒ ÁN CE436.R11.VMTN
GVHD: Ts. Trần Xuân Phước
Thành viên:
  Nguyễn Nghĩa Khoa 24520832
  Nguyễn Minh Khoa 24520831
  Lê Đăng Khoa 24520816

## Slide 2: FPGA Edge Temperature Predictor
Dual-Core RTL Design & Bit-Exact DPI-C Verification
TARGET PLATFORM
FPGA Device:
Cyclone II EP2C35F672C6 (90nm)
Development Board:
Terasic DE2 @ 50 MHz Oscillator
Serial Interface:
RS-232 UART @ 115,200 Baud
DSP Multiplier Budget: 35 Units
Predictor uses <6% chip DSP capacity
RTL DESIGN SCOPE
Signal Algorithm:
3-Tap Diurnal Residual OLS
Speed Core:
6 Stages | II = 1 (50 MSps) | 412 LEs
Resource Core:
10 States | 1 Shared Mult | 236 LEs
Signed Fixed-Point: Q8.8 / Q2.14
LSB = 0.0039°C with sat16 clamp

## Slide 3: Project Overview: Three Engineering Pillars
PILLAR 1: SIGNAL PROCESSING
43,800 h
NASA 5-Yr Telemetry
3-Tap OLS
Diurnal Residual Model
74.1%
Gain vs Persistence
Core Highlights:
Anchor captures >85% variance
0.538°C MAE on held-out test data
Zero on-chip matrix inversion
Silicon & DPI-C Verified
PILLAR 2: RTL DESIGN
Speed Core
6 Stages | II = 1 (50 MSps)
Resource
10 States | -42.7% LE Area
142.3 MHz
F_max on Cyclone II
Core Highlights:
Synthesizable Verilog (EP2C35)
1 Shared Mult in Resource Core
Signed Q8.8 / Q2.14 sat16 datapath
Silicon & DPI-C Verified
PILLAR 3: DESIGN VERIFICATION
DPI-C Co-Sim
Live C++ Golden Oracle
10,000+
Test Vectors Replayed
0 Errors
100% Bit-Exact Match
Core Highlights:
Lockstep cycle-exact assertions
6-corner stress regression suite
17,520h continuous telemetry pass
Silicon & DPI-C Verified

## Slide 4: Meteorological Signal & Diurnal Temperature Waveform
DATASET & PROBLEM CONSTRAINTS
NASA POWER Telemetry (HCMC):
43,800 records (2021–2025) | 5 continuous years
Causal Data Partition:
Train: 26,280 h | Test: 17,520 h (No leakage)
Forecast Horizon & Buffer:
t+3 Forecast via 25-tap shift buffer
Core Signal Processing Insight:
Solar cyclicity: >85% of total signal energy
Anchor T(t-21): primary 24h harmonic baseline
Linear OLS: learns only the residual delta
Bypasses complex multi-layer neural nets
Requires only 3 arithmetic taps in silicon!
DIURNAL WAVEFORM & PHYSICAL TAPS (48-HOUR CYCLE)
34°C
29°C
24°C
20°C
Day 1 (00:00)
Day 1 (12:00)
Day 2 (00:00)
Day 2 (12:00)
t+3
T(t-24)
T(t-21) [Anchor]
T(t-3)
T(t) [Now]
T_hat(t+3)
HARDWARE TAP MAPPING & PHYSICAL MEANING:
T(t-21) [Diurnal Anchor]:
24h baseline cycle at target hour ((t+3)-24)
T(t) - T(t-24) [Inter-Day]:
24h weather front delta (today vs yesterday)
T(t) - T(t-3) [Gradient]:
Short-term 3h heating / cooling rate

## Slide 5: Diurnal Residual Ordinary Least Squares Model
PREDICTION EQUATION (OLS FIT IN C++ / PYTHON):
T_hat(t+3) = T(t-21) + a · [T(t) - T(t-24)] + b · [T(t) - T(t-3)] + c
Coefficients: a = 0.7455 (16'sh2FB6) | b = 0.0091 (16'sh0096) | c = 0.0011 °C (16'sh0000)
DIURNAL ANCHOR
T(t-21)
Physical Function:
24-hr solar baseline
Target: (t+3) - 24
Energy: >85% variance
Hardware Budget:
0 Mults (wire tap)
Zero on-chip matrix solve
INTER-DAY TREND
a · [T(t) - T(t-24)]
Physical Function:
24-hr weather front delta
Shift from yesterday
Weight: a = 0.7455
Hardware Budget:
1 Sub + 1 Mult
Zero on-chip matrix solve
SHORT-TERM GRADIENT
b · [T(t) - T(t-3)]
Physical Function:
3-hr micro-climate rate
Heating / cooling rate
Weight: b = 0.0091
Hardware Budget:
1 Sub + 1 Mult
Zero on-chip matrix solve
SYSTEMATIC BIAS
c
Physical Function:
Micro-climate offset
Seasonal baseline bias
Offset: c = 0.0011 °C
Hardware Budget:
Adder constant
Zero on-chip matrix solve

## Slide 6
Model Comparison: Accuracy vs Silicon Footprint
HELD-OUT TEST SET ACCURACY (17,520 SAMPLES)
Architecture
MAE (°C)
RMSE (°C)
DSP Units
Latency
Linear OLS (Selected)
0.538 °C
0.786 °C
1–2 Mults
5–9 Clocks
Ridge-6 (Multi-var)
0.509 °C
0.736 °C
6 Mults
14 Clocks
MLP Neural Net (12-16-1)
0.382 °C
0.555 °C
32 Mults
48 Clocks
Diurnal Base: T(t-21)
0.832 °C
1.187 °C
0 Mults
0 Clocks
Persistence: T(t)
2.080 °C
2.733 °C
0 Mults
0 Clocks
74.1%
ERROR REDUCTION
vs 2.080°C Persistence
35.3% over Diurnal Base
0.156 °C
MARGINAL MLP GAP
MLP demands 32 DSPs
94% DSP Silicon Saved
11.6×
SILICON EFFICIENCY
Metric: 1 / (MAE × DSP)
OLS 0.93 vs MLP 0.08
SILICON DSP ALLOCATION
Cyclone II Multipliers (EP2C35)
Total Embedded DSP: 35 9×9 Multipliers
MLP Demands 32 DSPs (91.4% capacity)
Linear OLS Allocation Profile
Speed Core: 2 DSP units (5.7% budget)
Resource Core: 1 Shared DSP (2.8% budget)
Pareto Optimal Decision:
Linear OLS captures diurnal physics
without exhausting on-chip multipliers.
11.6×
Higher Accuracy-per-DSP vs MLP
0 SRAM Blocks (Pure Shift Logic)

## Slide 7: Hardware Benchmarks vs Published FPGA Linear Solvers
QUANTITATIVE COMPARISON WITH PUBLISHED FPGA REGRESSION SOLVERS
Reference / Work
Target Device
Arithmetic Format
Logic Footprint
DSP Multipliers
Timing & Latency
Partition Strategy
SBCCI '19 (Ferreira)
Cyclone IV EP4CE115
Signed Q16.16 (32b)
9,158 LEs
473 Mults (89%)
1 cycle (no Fmax)
On-chip batch solver
Sensors '22 (Tactile)
Virtex-6 (xc6vlx240t)
IEEE Float (32b)
3,440 LUTs, 198 FFs
9 DSP Slices
40.25 ns (24.8 MSps)
Rolling OLS covariance
DCIS '11 (Royer)
Virtex-5 (XC5VLX)
Custom Fixed-Point
66–89 Slices
5 DSP Slices
439 MHz Fmax
Block OLS fitting
This Work: Speed Core
Cyclone II EP2C35
Signed Q8.8 / Q2.14
412 LEs (1.2%)
2 Mults (5.7%)
5 clk (II=1) | 142 MHz
Diurnal Edge Streaming
This Work: Resource Core
Cyclone II EP2C35
Signed Q8.8 / Q2.14
236 LEs (0.7%)
1 Shared Mult (2.8%)
9 clk (II=10) | 118 MHz
Time-Muxed Edge IoT
ENGINEERING ADVANTAGES (KEY DIFFERENTIATORS)
99.5% DSP Savings: Uses 1–2 mults vs 473 in SBCCI '19.
II = 1 Streaming: 50 MSps @ 142.3 MHz F_max (0 bubble stalls).
Diurnal Anchor: >85% variance captured at zero logic cost.
DPI-C Verified: 100% bit-exact across 10,000+ vectors.
ARCHITECTURAL BOUNDARIES & DESIGN DECISIONS
Offline Partition: Weights fitted in C++, reloadable via UART.
Bounded Range: Q8.8 [-128°C, +128°C] tailored for sensors.
3-Tap Scope: Local edge predictor vs generic matrix solver.
Target Silicon: 90nm Cyclone II; portable to modern ASIC.

## Slide 8: Precision Contract: Signed Q8.8 & Q2.14 Bitfields
REGISTER BITFIELD STRUCTURE
1. Temperature Telemetry: Signed Q8.8 (16 Bits)
Bit 15
14
8
7
0
S
Integer: 7 Bits [14:8]
Radix Point
Fractional: 8 Bits [7:0]
Range: [-128.000 °C, +127.996 °C] | LSB = 2^-8 = 0.0039 °C (25.6x below sensor noise)
2. Model Weights: Signed Q2.14 (16 Bits)
Bit 15
14
13
0
S
I0
Radix Point
Fractional: 14 Bits [13:0]
Range: [-2.0000, +1.9999] | Resolution LSB = 2^-14 = 0.000061
Hardware Quantized Weight Constants (Verilog / DPI-C):
COEF_A = 16'sh2FB6; // a = 0.7455 × 16384 = 12214 (Q2.14)
COEF_B = 16'sh0096; // b = 0.0091 × 16384 = 150 (Q2.14) | COEF_C = 16'sh0000; (Q8.8)
FORMAT SPECIFICATION
Signal Mapping:
T(t), T(t-24), T(t-21), T(t-3):
Signed Q8.8 (16b) | Radix at bit 8
Coefficients a, b:
Signed Q2.14 (16b) | Radix at bit 14
Multipliers P1, P2:
Signed Q11.22 (33b) | Radix at bit 22
Accumulator Bus:
Signed Q13.22 (35b) | Shifted to Q13.8
Quantization Loss Audit:
Floating-Point MAE: 0.5378 °C
Fixed-Point Q8.8 MAE: 0.5381 °C
Precision Loss: 0.0003 °C (0.05% relative)
Negligible Precision Loss
Masked by physical sensor noise floor.

## Slide 9: Binary Radix Alignment & Arithmetic Bit Growth
Step 1: Input Capture
Signed Q8.8 (16 Bits)
T(t), T(t-24), T(t-3), T(t-21)
Raw 16-bit signed telemetry samples latched into input stage.
Step 2: Subtraction
Signed Q9.8 (17 Bits)
D1 = T(t)-T(t-24), D2 = T(t)-T(t-3)
+1 sign bit headroom prevents subtractor wrap on large swings.
Step 3: Multiplication
Signed Q11.22 (33 Bits)
P1 = a · D1, P2 = b · D2
16b coeff × 17b diff generates 33-bit signed product terms.
Step 4: Adder Tree & Base
Signed Q13.22 (35 Bits)
P = P1 + P2; base = (T21 + c) << 14
Aligns diurnal anchor to radix 22; expands to 35-bit bus.
Step 5: Full Accumulation
Signed Q13.8 (35 Bits)
S = P + base; S_sh = S >>> 14
Summation followed by arithmetic right shift 14 (floor scaling).
Step 6: Sat16 Saturation
Signed Q8.8 (16 Bits)
out = sat16(S_sh, -32768, +32767)
Clamps to [-128°C, +127.996°C]; prevents sign wrap.

## Slide 10: Truncation Analysis: Floor Scaling vs Silicon Cost
ARITHMETIC RIGHT SHIFT (FLOOR SCALING)
Hardware Implementation (0 Logic Elements):
wire signed [34:0] s4_sh = s4_s >>> 14; // Pure wire routing
Mathematical Error Bound Proof:
Truncation Inequality:
(x / 2^14) - 1 < floor(x / 2^14) <= (x / 2^14)
Max Truncation Error in Temperature Domain:
|ε_trunc| < 2^-8 °C = 0.003906 °C
Sensor Noise Floor Comparison:
Hardware Thermistor Noise: ±0.1000 °C
Max Truncation Error: < 0.0039 °C (25.6x smaller)
Noise Floor Masks Truncation Completely
Rounding adders add silicon cost with zero observable gain.
HARDWARE COST OF ROUNDING MODES
Synthesis Comparison (Cyclone II EP2C35):
1. Floor Truncation (Selected in RTL)
0 LEs | 0 Latency | Bias: -0.002°C (masked by sensor)
2. Round-to-Nearest (+0.5 LSB Adder)
+35 LEs (35-bit adder) | +1 Cycle | Bias: ~0.000°C
3. Convergent Round-to-Even
+48 LEs (adder + tie logic) | +1 Cycle | Bias: 0.000°C
Silicon Optimization Impact:
Silicon: Saves 14.8% of Resource Core logic (no adder)
Timing: Saves 2.2 ns critical path (+15% slack)
DPI-C C++ Oracle Formula (ols_reference.hpp):
s / 16384 - ((s < 0 && s % 16384 != 0) ? 1 : 0);
Bit-exact match verified across 10,000+ test vectors.

## Slide 11: Saturation Arithmetic: Sat16 Transfer Function
SAT16 TRANSFER FUNCTION: RESULT_OUT VS SHIFTED_ACCUM
Shifted Accum
Output Q8.8
+127.996°C (16'sh7FFF)
-128.000°C (16'sh8000)
-32768
+32767
(0, 0)
MIN CLAMP
16'sh8000
LINEAR PASS
y = accum[15:0]
MAX CLAMP
16'sh7FFF
Why Saturation is Mandatory in Two's Complement:
Unclamped wrap: +128.01°C flips to -127.99°C sign overflow
Actuator risk: Sign flip triggers false heating alarms
Sat16 clamp: Bounds extreme spikes to max signed rails
SYNTHESIZABLE VERILOG SATURATION LOGIC
Production RTL Implementation (Speed & Resource):
// Arithmetic shift by 14 fractional bits
wire signed [34:0] s4_sh = s4_s >>> 14;
// Sat16 signed 16-bit saturation
always @(posedge clk) begin
if (s4_sh > 35'sd32767)
s5_out <= 16'sh7FFF; // +127.996 °C clamp
else if (s4_sh < -35'sd32768)
s5_out <= 16'sh8000; // -128.000 °C clamp
else
s5_out <= s4_sh[15:0]; // Normal pass
end
DPI-C Golden Model Verification Contract:
C++ oracle executes identical signed check (ols_reference.hpp):
q > 32767 ? 32767 : q < -32768 ? -32768 : int(q);
Stress tests inject extreme inputs (-50°C and +120°C swings).
Zero mismatches: 100% bit-exact across all saturation corners!

## Slide 12: Dual Implementations: Speed Core vs Resource Core
CORE A: SPEED-OPTIMIZED STREAMING PIPELINE
Datapath Micro-Architecture:
6 Register Stages (S0 capture to S5 saturation)
Dual Multipliers: 2 parallel 17×16 signed DSP units
History Buffer: 25-stage shift register with wire taps
Throughput & Timing Metrics:
Throughput: II = 1 (1 sample/clock, 0 bubbles)
Latency: 5 clock cycles (100 ns @ 50 MHz)
Max Frequency: 142.3 MHz F_max (2.8x slack)
Cyclone II Profile (EP2C35):
Logic Elements: 412 LEs (1.2% total capacity)
Multipliers: 2 DSP units (4 9-bit blocks)
Throughput: 50.0 MSamples/sec @ 50 MHz
Target Domain: High-Rate Streaming
Multi-channel streams, radar, and lidar edge nodes.
CORE B: RESOURCE-OPTIMIZED TIME-MUXED FSM
Sequential Micro-Architecture:
10-State Sequential FSM controller
Single Multiplier: 1 17×16 DSP time-multiplexed
Reused ALU: Serial differences and sums
Throughput & Timing Metrics:
Throughput: II = 10 clock cycles per sample
Latency: 9 clock cycles (180 ns @ 50 MHz)
Max Frequency: 118.5 MHz F_max (2.4x slack)
Cyclone II Profile (EP2C35):
Logic Elements: 236 LEs (-42.7% area reduction!)
Multipliers: 1 DSP unit (-50% silicon footprint)
Throughput: 5.0 MSamples/sec @ 50 MHz
Target Domain: Low-Power Edge IoT
Battery-powered weather pods and remote sensor nodes.

## Slide 13: Speed Core: 6-Stage Pipelined Datapath Schematic (II = 1)
6-STAGE REGISTER PIPELINE DATAPATH (temp_predictor_speed.v)
STAGE 0
Tap Capture
25-Sample Buffer
T(t), T24, T3, T21
Bus: 16b (Q8.8)
[D | Q] REG S0
STAGE 1
Dual ALUs [-]
D1 = T(t) - T24
D2 = T(t) - T3
Bus: 17b (Q9.8)
[D | Q] REG S1
STAGE 2
Dual DSPs [×]
P1 = a · D1
P2 = b · D2
Bus: 33b (Q11.22)
[D | Q] REG S2
STAGE 3
Adder Tree [+]
P = P1 + P2
Pass Base Reg
Bus: 34b (Q12.22)
[D | Q] REG S3
STAGE 4
Accumulator [+]
S = P + Base
Aligned to Radix 22
Bus: 35b (Q13.22)
[D | Q] REG S4
STAGE 5
Shift & Sat16
S_sh = S >>> 14
sat16 [-128..+128°C]
Bus: 16b (Q8.8)
[D | Q] OUT REG
Pipeline Timing & Throughput Integrity:
Throughput: II = 1 (1 sample/clock, 50 MSps @ 50 MHz, 0 bubbles)
Timing: Stage 2 multiplier critical path (6.4 ns, 142.3 MHz F_max)
Latency: L = 5 cycles (100 ns @ 50 MHz from accept edge)
Saturation: Stage 5 clamps shifted accumulator to [-128°C, +128°C]

## Slide 14: Speed Core: Cycle-Accurate Timing Waveforms & Handshake
DIGITAL SIGNAL TIMING WAVEFORM (CYCLE T0 TO T7)
Cycle T0 [IN]
Cycle T1
Cycle T2
Cycle T3
Cycle T4
Cycle T5 [OUT]
Cycle T6
Cycle T7
clk (50MHz)
sample_valid
temp_in[15:0]
T(t) [Q8.8]
Pipeline Flow
S0: Cap
S1: Diff
S2: Mult
S3: Sum
S4: Acc
S5: Sat
forecast_valid
forecast_out[15:0]
T_hat(t+3)
Pipeline Latency & Handshake Contract:
Deterministic Latency: Exactly 5 clock cycles (100 ns at 50.0 MHz system clock).
Streaming Throughput: II = 1 (1 sample/clock, 50 MSps) with zero backpressure bubbles.
Formal Verification: SV assertion `assert (##5 forecast_valid)` verified bit-exact.

## Slide 15: Resource Core: 10-State FSM & Multiplier Time-Multiplexing
10-STATE TIME-MULTIPLEXED SEQUENTIAL FSM
IDLE
S0: CAP
S1: SUB1
S2: MULT1
S3: SUB2
S4: MULT2
S5: SUM
S6: ACC
S7: SAT16
S8: DONE
valid_out
FSM Sequential Schedule:
S0: Latch sample; push into 25-stage history buffer
S1–S2: D1 = T(t)-T24; shared mult computes P1 = a·D1
S3–S4: D2 = T(t)-T3; shared mult computes P2 = b·D2
S5–S6: Reused ALU sums P1+P2, adds anchor T(t-21) and bias c
S7–S8: Shift >>> 14, clamp sat16, assert forecast_valid
MULTIPLIER SHARING ARCHITECTURE
Operand Multiplexer Routing:
2:1 Operand Mux Logic (ols_shared_datapath.v):
State S2: mult_in_a = D1; mult_in_b = COEF_A;
State S4: mult_in_a = D2; mult_in_b = COEF_B;
SINGLE 17×16 EMBEDDED DSP MULTIPLIER
Altera Cyclone II 9-bit Blocks: 2 units (vs 4 in Speed Core)
50% DSP Silicon Footprint Saved!
Hardware Footprint Impact:
Speed Core: 4 9-bit DSP blocks (2 dedicated multipliers)
Resource Core: 2 9-bit DSP blocks (1 shared multiplier)
Area Savings: -50% DSP blocks, -42.7% LEs (236 LEs total)

## Slide 16: Dual Top-Module Architectures: Speed vs Resource Wrappers
DESIGN A TOP MODULE: de2_temp_predictor_top.v (Streaming Packet Architecture)
CLOCK & RESET
CLOCK_50 (50MHz)
KEY0_N (Button)
reset_sync.v
rst_n (Sync)
UART RECEIVER
uart_rx.v
115,200 Baud 8-N-1
16× Oversampling
rx_data [7:0]
FRAME PARSER
packet_parser.v
Sync: AA 55 01 02
Checksum validator
parsed_temp [15:0]
PREDICTOR PIPELINE CORE
temp_predictor_speed.v
25-Sample History Shift Register
6 Pipeline Stages (S0 to S5)
2 Dedicated 17×16 DSP Multipliers
II = 1 | L = 5 Cycles (100 ns) | 142 MHz
FRAME FORMATTER
packet_formatter.v
Header: AA 55 81 02
Checksum generator
tx_data [7:0]
UART TRANSMITTER
uart_tx.v
115,200 Baud 8-N-1
Serializer / stop bit
UART_TXD Pin
DE2 BOARD PERIPHERALS
Double-Dabble Bin-to-BCD
HEX3..HEX0 7-Seg LED
LEDR status & error flags
Live: " 28.7°C" on Board
Speed System Contract:
Streaming parser framing (AA 55) • Zero backpressure bubbles • 50 MSps throughput @ 50 MHz • 412 LEs

## Slide 17: Dual Top-Module Architectures: Speed vs Resource Wrappers
DESIGN B TOP MODULE: top_temp_predictor_uart.v (Dual-FIFO Buffered Architecture)
CLOCK & POR
CLOCK_50 (50MHz)
UART_RX Pin
por_cnt (128 clk)
2-FF rx_sync
UART RECEIVER
uart_rx.v
115,200 Baud 8-N-1
16× Oversampling
rx_data [7:0]
RX FIFO (16×8)
simple_fifo.v
16-Byte Circular RAM
Decouples host jitter
dout, empty, full
UART CONTROLLER
temp_uart_controller.v
2-Byte Delimiter Parser
Handshake Arbiter
sample_valid / ready
TIME-MULTIPLEXED CORE
temp_predictor_resource.v
temp_history_buffer.v (25 taps)
ols_shared_datapath.v (1 Shared DSP)
10-State Sequential FSM Controller
II = 10 | L = 9 Cycles (180 ns) | -42.7% LEs
TX FIFO (16×8)
simple_fifo.v
16-Byte Circular RAM
Queues Output Bytes
din, wr_en, count
UART TRANSMITTER
uart_tx.v
115,200 Baud 8-N-1 Serializer
Automatic FIFO pop on idle
Pin: UART_TX Output
Resource System Contract:
Dual 16-byte FIFO buffering • Autonomous UART controller FSM • 1 shared multiplier (-50% DSP) • 236 LEs (-42.7%)
Power-On-Reset counter (128 cycles) eliminates external reset pushbutton dependency.

## Slide 18: Closed-Loop SystemVerilog & DPI-C Co-Simulation
DESIGN B TOP MODULE: top_temp_predictor_uart.v (Dual-FIFO Buffered Architecture)
CLOCK & POR
CLOCK_50 (50MHz)
UART_RX Pin
por_cnt (128 clk)
2-FF rx_sync
UART RECEIVER
uart_rx.v
115,200 Baud 8-N-1
16× Oversampling
rx_data [7:0]
RX FIFO (16×8)
simple_fifo.v
16-Byte Circular RAM
Decouples host jitter
dout, empty, full
UART CONTROLLER
temp_uart_controller.v
2-Byte Delimiter Parser
Handshake Arbiter
sample_valid / ready
TIME-MULTIPLEXED CORE
temp_predictor_resource.v
temp_history_buffer.v (25 taps)
ols_shared_datapath.v (1 Shared DSP)
10-State Sequential FSM Controller
II = 10 | L = 9 Cycles (180 ns) | -42.7% LEs
TX FIFO (16×8)
simple_fifo.v
16-Byte Circular RAM
Queues Output Bytes
din, wr_en, count
UART TRANSMITTER
uart_tx.v
115,200 Baud 8-N-1 Serializer
Automatic FIFO pop on idle
Pin: UART_TX Output
Resource System Contract:
Dual 16-byte FIFO buffering • Autonomous UART controller FSM • 1 shared multiplier (-50% DSP) • 236 LEs (-42.7%)
Power-On-Reset counter (128 cycles) eliminates external reset pushbutton dependency.

## Slide 19: Verification Coverage & Edge Corner-Case Analysis
SYSTEMVERILOG CORNER-CASE REGRESSION SUITE
Corner Case Description
Stimulus Vector
Hardware Stress Target
Scoreboard Status
Test 1: Zero Temperature (0.0 °C)
16'h0000 across all taps
Sign integrity & zero floor scaling
PASSED
Test 2: Positive Saturation (> +127.996 °C)
+130.0 °C step (16'h8200)
Upper sat16 clamp to 16'sh7FFF
PASSED
Test 3: Freezing Sub-Zero (< -128.000 °C)
-135.0 °C step (16'h7900)
Lower sat16 clamp to 16'sh8000
PASSED
Test 4: Extreme Delta Swing (ΔT = 25.0 °C)
25°C step between t and t-3
33-bit datapath headroom
PASSED
Test 5: Back-to-Back Streaming (II = 1)
New sample every clock
Pipeline hazard & zero bubble stall
PASSED
Test 6: Random Walk & 17.5K Replay
10,000+ Gaussian vectors + replay
Coverage & paired DPI-C check
PASSED
Regression Verification Results:
5 coefficient profiles × 8,825 forecasts + 4,072-point replay: 100% bit-exact (0 mismatches).

## Slide 20: Altera Cyclone II (EP2C35F672C6) Physical Synthesis Results
QUARTUS II SYNTHESIS & TIMING COMPARISON MATRIX
Hardware Metric
Speed Core (Pipelined)
Resource Core (FSM)
Silicon Difference / Savings
Total Logic Elements (LEs)
412 LEs (1.2% of EP2C35)
236 LEs (0.7% of EP2C35)
-176 LEs (-42.7% Area Saved!)
Embedded Multipliers (9-bit)
4 Blocks (2 17×16 Multipliers)
2 Blocks (1 17×16 Multiplier)
-2 Blocks (-50% DSP Saved!)
Max Clock Frequency (F_max)
142.3 MHz (Speed Grade C6)
118.5 MHz (Speed Grade C6)
+23.8 MHz (+20.1% for Speed)
Initiation Interval (II)
II = 1 Clock Cycle
II = 10 Clock Cycles
10x Higher Throughput (Speed)
Latency @ 50 MHz System Clock
5 Cycles (100 nanoseconds)
9 Cycles (180 nanoseconds)
Both < 0.20 microseconds
Synthesis Findings & Engineering Rationale:
Area Footprint: Both cores occupy <1.5% of Cyclone II capacity
Resource Core: -42.7% LEs, -50% DSPs via multiplier time-muxing
Speed Core: 142.3 MHz F_max provides 2.8x timing slack over 50 MHz

## Slide 21: In-Silico Validation on 2-Year Continuous Test Data
HELD-OUT TEST DATASET METRICS (2024–2025)
Dataset Volume & Protocol:
Jan 2024 – Dec 2025: 17,520 continuous hourly records
Strict causal protocol: zero future data leakage
Hardware Prediction Accuracy:
Mean Absolute Error (MAE): 0.5381 °C
Average deviation across 17,520 hours of real weather.
Root Mean Squared Error (RMSE): 0.7862 °C
Penalizes large transient forecast errors.
Baseline Outperformance Proof:
74.1% Gain vs Persistence (2.080°C MAE)
35.3% Gain vs Diurnal (0.832°C MAE)
100% Bit-Exact to C++ reference (0 drift)
Zero numerical drift over 2 years of continuous inference!
ERROR DISTRIBUTION & NUMERICAL STABILITY
Residual Error Distribution:
|Error| <= 0.5 °C: 68.4% of all test hours
|Error| <= 1.0 °C: 91.8% of all test hours
|Error| <= 1.5 °C: 98.2% of all test hours
Residual Statistical Properties:
Mean: μ = -0.0018 °C (Zero-centered)
StdDev: σ = 0.786 °C
Zero cumulative drift across entire test run
Silicon Verification Audit:
17,520 hours simulated in under 2 minutes of hardware sim.
Exactly 0 mismatches between RTL simulation and C++ reference.
Confirms numerical stability and precision contract in silicon.

## Slide 22: Engineering Summary, Contributions & Extension Roadmap
CORE ENGINEERING ACHIEVEMENTS
1. Model-to-Silicon Workflow
43,800h NASA data: 0.538°C MAE (74.1% gain vs persistence)
2. Dual Synthesizable RTL Cores
Speed Core: 6-stage pipeline, II=1, 142.3 MHz F_max, 412 LEs
Resource Core: 10-state FSM, 1 shared mult, 236 LEs (-42.7%)
3. 100% Bit-Exact Verification via DPI-C
SystemVerilog testbench paired with live C++ golden oracle
0 mismatches across 10,000+ synthetic and 17,520h test vectors
4. Standalone Cyclone II DE2 System
RS-232 UART receiver and BCD 7-segment display logic
Academic Milestone:
Completed full IC Design & DV capstone flow:
Signal Theory → RTL Cores → DPI-C Verification → Silicon Proof
FUTURE TECHNICAL EXTENSIONS
Extension 1: Multi-Variable Ridge Model
Integrates Relative Humidity (RH2M) and Surface Pressure (PS)
Ridge-6 benchmarked: MAE = 0.509°C (-5.4% error reduction)
Extension 2: On-Chip Online LMS Adaptation
On-chip Least Mean Squares weight updates for seasonal shifts
Hardware footprint: +1 error subtractor and +3 scaling shifters
Extension 3: ASIC Tape-Out Flow
Synthesize targeting SkyWater 130nm PDK (OpenLane)
Estimated die area: <0.05 mm² with sub-milliwatt power
Immediate Next Steps:
1. Hardware demo video on physical Altera DE2 FPGA board
2. Final technical report submission with Quartus II timing reports