## Slide 1
CE436: DISCRETE-TIME SIGNAL PROCESSING & APPLICATIONS
FPGA Edge Temperature Predictor
Dual-Core RTL Design & Bit-Exact DPI-C Verification
Altera Cyclone II (DE2) | Signed Q8.8 / Q2.14 | 50 MHz Real-Time Inference
100% BIT-EXACT MATCH (10,000+ VECTORS)
TARGET PLATFORM
FPGA Device:
Cyclone II EP2C35F672C6 (90nm)
Development Board:
Terasic DE2 @ 50 MHz Oscillator
Serial Interface:
RS-232 UART @ 115,200 Baud
DSP Multiplier Budget: 35 Units
Predictor uses <6% chip DSP capacity
RTL DESIGN SCOPE
Signal Algorithm:
3-Tap Diurnal Residual OLS
Speed Core:
6 Stages | II = 1 (50 MSps) | 412 LEs
Resource Core:
10 States | 1 Shared Mult | 236 LEs
Signed Fixed-Point: Q8.8 / Q2.14
LSB = 0.0039°C with sat16 clamp
DEFENSE METADATA
Student Engineers:
Le Dang Khoa (24520816) — Lead / RTL
Nguyen Nghia Khoa (24520832) — Model
Nguyen Minh Khoa (24520831) — DV / TB
Academic Advisor:
Dr. Tran Xuan Phuoc (CE-UIT)
Status: 100% Bit-Exact Match
0 Mismatches across 10,000+ vectors

## Slide 2
FULL-STACK IC DESIGN
Project Overview: Three Engineering Pillars
Signal theory, synthesizable RTL micro-architecture, and closed-loop DV
PILLAR 1: SIGNAL PROCESSING
43,800 h
NASA 5-Yr Telemetry
3-Tap OLS
Diurnal Residual Model
74.1%
Gain vs Persistence
Core Highlights:
Anchor captures >85% variance
0.538°C MAE on held-out test data
Zero on-chip matrix inversion
Silicon & DPI-C Verified
PILLAR 2: RTL DESIGN
Speed Core
6 Stages | II = 1 (50 MSps)
Resource
10 States | -42.7% LE Area
142.3 MHz
F_max on Cyclone II
Core Highlights:
Synthesizable Verilog (EP2C35)
1 Shared Mult in Resource Core
Signed Q8.8 / Q2.14 sat16 datapath
Silicon & DPI-C Verified
PILLAR 3: DESIGN VERIFICATION
DPI-C Co-Sim
Live C++ Golden Oracle
10,000+
Test Vectors Replayed
0 Errors
100% Bit-Exact Match
Core Highlights:
Lockstep cycle-exact assertions
6-corner stress regression suite
17,520h continuous telemetry pass
Silicon & DPI-C Verified
CE436 CAPSTONE
End-to-end flow: diurnal signal model, dual RTL cores, and bit-exact DPI-C verification.

## Slide 3
DEFENSE OUTLINE
Capstone Defense Agenda
Structured overview of signal modeling, fixed-point math, dual architectures, and silicon verification
01
Signal Formulation & Prior Art
NASA 5-yr data, diurnal equation, and benchmarks
02
Fixed-Point Precision Contract
Signed Q8.8/Q2.14, bit growth, and sat16 clamping
03
Dual RTL Micro-Architectures
Speed Core (II=1) vs Resource Core (1 shared mult)
04
Top-Level Integration & IO
Cyclone II DE2 mapping, RS-232 UART, and 7-segment LEDs
05
Bit-Exact DPI-C Verification
SystemVerilog testbench, C++ oracle, and regressions
06
Silicon Synthesis & Validation
Quartus II EP2C35 results and 17,520h test replay
CE436 CAPSTONE
Six sections covering theory, arithmetic, micro-architecture, and silicon proof.

## Slide 4
SIGNAL CHARACTERISTICS & PROBLEM FORMULATION
Meteorological Signal & Diurnal Temperature Waveform
Exploiting 24-hour solar cyclicity from NASA POWER satellite observations in Ho Chi Minh City
DATASET & PROBLEM CONSTRAINTS
NASA POWER Telemetry (HCMC):
43,800 records (2021–2025) | 5 continuous years
Causal Data Partition:
Train: 26,280 h | Test: 17,520 h (No leakage)
Forecast Horizon & Buffer:
t+3 Forecast via 25-tap shift buffer
Core Signal Processing Insight:
Solar cyclicity: >85% of total signal energy
Anchor T(t-21): primary 24h harmonic baseline
Linear OLS: learns only the residual delta
Bypasses complex multi-layer neural nets
Requires only 3 arithmetic taps in silicon!
DIURNAL WAVEFORM & PHYSICAL TAPS (48-HOUR CYCLE)
34°C
29°C
24°C
20°C
Day 1 (00:00)
Day 1 (12:00)
Day 2 (00:00)
Day 2 (12:00)
t+3
T(t-24)
T(t-21) [Anchor]
T(t-3)
T(t) [Now]
T_hat(t+3)
HARDWARE TAP MAPPING & PHYSICAL MEANING:
T(t-21) [Diurnal Anchor]:
24h baseline cycle at target hour ((t+3)-24)
T(t) - T(t-24) [Inter-Day]:
24h weather front delta (today vs yesterday)
T(t) - T(t-3) [Gradient]:
Short-term 3h heating / cooling rate
CE436 CAPSTONE
Diurnal anchor T(t-21) captures 24h baseline; 2 delta taps fit residual dynamics with only 2 multipliers.

## Slide 5
MATHEMATICAL RESIDUAL FORMULATION
Diurnal Residual Ordinary Least Squares Model
Decomposing temperature dynamics into diurnal baseline, inter-day trend, and rate-of-change
PREDICTION EQUATION (OLS FIT IN C++ / PYTHON):
T_hat(t+3) = T(t-21) + a · [T(t) - T(t-24)] + b · [T(t) - T(t-3)] + c
Coefficients: a = 0.7455 (16'sh2FB6) | b = 0.0091 (16'sh0096) | c = 0.0011 °C (16'sh0000)
DIURNAL ANCHOR
T(t-21)
Physical Function:
24-hr solar baseline
Target: (t+3) - 24
Energy: >85% variance
Hardware Budget:
0 Mults (wire tap)
Zero on-chip matrix solve
INTER-DAY TREND
a · [T(t) - T(t-24)]
Physical Function:
24-hr weather front delta
Shift from yesterday
Weight: a = 0.7455
Hardware Budget:
1 Sub + 1 Mult
Zero on-chip matrix solve
SHORT-TERM GRADIENT
b · [T(t) - T(t-3)]
Physical Function:
3-hr micro-climate rate
Heating / cooling rate
Weight: b = 0.0091
Hardware Budget:
1 Sub + 1 Mult
Zero on-chip matrix solve
SYSTEMATIC BIAS
c
Physical Function:
Micro-climate offset
Seasonal baseline bias
Offset: c = 0.0011 °C
Hardware Budget:
Adder constant
Zero on-chip matrix solve
CE436 CAPSTONE
OLS formulation isolates 3 simple operations: 2 subtractions, 2 multiplications, and a base addition.

## Slide 6
ALGORITHMIC BENCHMARKS & PARETO FRONTIER
Model Comparison: Accuracy vs Silicon Footprint
Held-out test dataset (17,520 hours) evaluating predictive accuracy against DSP demand
HELD-OUT TEST SET ACCURACY (17,520 SAMPLES)
Architecture
MAE (°C)
RMSE (°C)
DSP Units
Latency
Linear OLS (Selected)
0.538 °C
0.786 °C
1–2 Mults
5–9 Clocks
Ridge-6 (Multi-var)
0.509 °C
0.736 °C
6 Mults
14 Clocks
MLP Neural Net (12-16-1)
0.382 °C
0.555 °C
32 Mults
48 Clocks
Diurnal Base: T(t-21)
0.832 °C
1.187 °C
0 Mults
0 Clocks
Persistence: T(t)
2.080 °C
2.733 °C
0 Mults
0 Clocks
74.1%
ERROR REDUCTION
vs 2.080°C Persistence
35.3% over Diurnal Base
0.156 °C
MARGINAL MLP GAP
MLP demands 32 DSPs
94% DSP Silicon Saved
11.6×
SILICON EFFICIENCY
Metric: 1 / (MAE × DSP)
OLS 0.93 vs MLP 0.08
SILICON DSP ALLOCATION
Cyclone II Multipliers (EP2C35)
Total Embedded DSP: 35 9×9 Multipliers
MLP Demands 32 DSPs (91.4% capacity)
Linear OLS Allocation Profile
Speed Core: 2 DSP units (5.7% budget)
Resource Core: 1 Shared DSP (2.8% budget)
Pareto Optimal Decision:
Linear OLS captures diurnal physics
without exhausting on-chip multipliers.
11.6×
Higher Accuracy-per-DSP vs MLP
0 SRAM Blocks (Pure Shift Logic)
CE436 CAPSTONE
Linear OLS achieves 0.538°C MAE with 94% fewer multipliers than deep learning.

## Slide 7
PRIOR ART & LITERATURE COMPARISON
Hardware Benchmarks vs Published FPGA Linear Solvers
Silicon area, DSP multiplier count, and streaming throughput comparison
QUANTITATIVE COMPARISON WITH PUBLISHED FPGA REGRESSION SOLVERS
Reference / Work
Target Device
Arithmetic Format
Logic Footprint
DSP Multipliers
Timing & Latency
Partition Strategy
SBCCI '19 (Ferreira)
Cyclone IV EP4CE115
Signed Q16.16 (32b)
9,158 LEs
473 Mults (89%)
1 cycle (no Fmax)
On-chip batch solver
Sensors '22 (Tactile)
Virtex-6 (xc6vlx240t)
IEEE Float (32b)
3,440 LUTs, 198 FFs
9 DSP Slices
40.25 ns (24.8 MSps)
Rolling OLS covariance
DCIS '11 (Royer)
Virtex-5 (XC5VLX)
Custom Fixed-Point
66–89 Slices
5 DSP Slices
439 MHz Fmax
Block OLS fitting
This Work: Speed Core
Cyclone II EP2C35
Signed Q8.8 / Q2.14
412 LEs (1.2%)
2 Mults (5.7%)
5 clk (II=1) | 142 MHz
Diurnal Edge Streaming
This Work: Resource Core
Cyclone II EP2C35
Signed Q8.8 / Q2.14
236 LEs (0.7%)
1 Shared Mult (2.8%)
9 clk (II=10) | 118 MHz
Time-Muxed Edge IoT
ENGINEERING ADVANTAGES (KEY DIFFERENTIATORS)
99.5% DSP Savings: Uses 1–2 mults vs 473 in SBCCI '19.
II = 1 Streaming: 50 MSps @ 142.3 MHz F_max (0 bubble stalls).
Diurnal Anchor: >85% variance captured at zero logic cost.
DPI-C Verified: 100% bit-exact across 10,000+ vectors.
ARCHITECTURAL BOUNDARIES & DESIGN DECISIONS
Offline Partition: Weights fitted in C++, reloadable via UART.
Bounded Range: Q8.8 [-128°C, +128°C] tailored for sensors.
3-Tap Scope: Local edge predictor vs generic matrix solver.
Target Silicon: 90nm Cyclone II; portable to modern ASIC.
CE436 CAPSTONE
Offline weight fitting reduces DSP footprint by 99.5% while sustaining II=1 throughput.

## Slide 8
FIXED-POINT QUANTIZATION ARCHITECTURE
Precision Contract: Signed Q8.8 & Q2.14 Bitfields
Eliminating floating-point silicon overhead via two's complement integer arithmetic
REGISTER BITFIELD STRUCTURE
1. Temperature Telemetry: Signed Q8.8 (16 Bits)
Bit 15
14
8
7
0
S
Integer: 7 Bits [14:8]
Radix Point
Fractional: 8 Bits [7:0]
Range: [-128.000 °C, +127.996 °C] | LSB = 2^-8 = 0.0039 °C (25.6x below sensor noise)
2. Model Weights: Signed Q2.14 (16 Bits)
Bit 15
14
13
0
S
I0
Radix Point
Fractional: 14 Bits [13:0]
Range: [-2.0000, +1.9999] | Resolution LSB = 2^-14 = 0.000061
Hardware Quantized Weight Constants (Verilog / DPI-C):
COEF_A = 16'sh2FB6; // a = 0.7455 × 16384 = 12214 (Q2.14)
COEF_B = 16'sh0096; // b = 0.0091 × 16384 = 150 (Q2.14) | COEF_C = 16'sh0000; (Q8.8)
FORMAT SPECIFICATION
Signal Mapping:
T(t), T(t-24), T(t-21), T(t-3):
Signed Q8.8 (16b) | Radix at bit 8
Coefficients a, b:
Signed Q2.14 (16b) | Radix at bit 14
Multipliers P1, P2:
Signed Q11.22 (33b) | Radix at bit 22
Accumulator Bus:
Signed Q13.22 (35b) | Shifted to Q13.8
Quantization Loss Audit:
Floating-Point MAE: 0.5378 °C
Fixed-Point Q8.8 MAE: 0.5381 °C
Precision Loss: 0.0003 °C (0.05% relative)
Negligible Precision Loss
Masked by physical sensor noise floor.
CE436 CAPSTONE
Strict Q8.8 and Q2.14 precision contracts eliminate floating-point logic while incurring only 0.0003°C error.

## Slide 9
DATAPATH WORDLENGTH EVOLUTION
Binary Radix Alignment & Arithmetic Bit Growth
Tracking wordlength expansion through subtraction, multiplication, accumulation, and saturation
Step 1: Input Capture
Signed Q8.8 (16 Bits)
T(t), T(t-24), T(t-3), T(t-21)
Raw 16-bit signed telemetry samples latched into input stage.
Step 2: Subtraction
Signed Q9.8 (17 Bits)
D1 = T(t)-T(t-24), D2 = T(t)-T(t-3)
+1 sign bit headroom prevents subtractor wrap on large swings.
Step 3: Multiplication
Signed Q11.22 (33 Bits)
P1 = a · D1, P2 = b · D2
16b coeff × 17b diff generates 33-bit signed product terms.
Step 4: Adder Tree & Base
Signed Q13.22 (35 Bits)
P = P1 + P2; base = (T21 + c) << 14
Aligns diurnal anchor to radix 22; expands to 35-bit bus.
Step 5: Full Accumulation
Signed Q13.8 (35 Bits)
S = P + base; S_sh = S >>> 14
Summation followed by arithmetic right shift 14 (floor scaling).
Step 6: Sat16 Saturation
Signed Q8.8 (16 Bits)
out = sat16(S_sh, -32768, +32767)
Clamps to [-128°C, +127.996°C]; prevents sign wrap.
CE436 CAPSTONE
Explicit bit-growth tracking guarantees zero unhandled arithmetic overflow before final saturation clamping.

## Slide 10
ROUNDING ARCHITECTURE & NOISE BOUND
Truncation Analysis: Floor Scaling vs Silicon Cost
Bounded truncation error and silicon cost vs rounding alternatives
ARITHMETIC RIGHT SHIFT (FLOOR SCALING)
Hardware Implementation (0 Logic Elements):
wire signed [34:0] s4_sh = s4_s >>> 14; // Pure wire routing
Mathematical Error Bound Proof:
Truncation Inequality:
(x / 2^14) - 1 < floor(x / 2^14) <= (x / 2^14)
Max Truncation Error in Temperature Domain:
|ε_trunc| < 2^-8 °C = 0.003906 °C
Sensor Noise Floor Comparison:
Hardware Thermistor Noise: ±0.1000 °C
Max Truncation Error: < 0.0039 °C (25.6x smaller)
Noise Floor Masks Truncation Completely
Rounding adders add silicon cost with zero observable gain.
HARDWARE COST OF ROUNDING MODES
Synthesis Comparison (Cyclone II EP2C35):
1. Floor Truncation (Selected in RTL)
0 LEs | 0 Latency | Bias: -0.002°C (masked by sensor)
2. Round-to-Nearest (+0.5 LSB Adder)
+35 LEs (35-bit adder) | +1 Cycle | Bias: ~0.000°C
3. Convergent Round-to-Even
+48 LEs (adder + tie logic) | +1 Cycle | Bias: 0.000°C
Silicon Optimization Impact:
Silicon: Saves 14.8% of Resource Core logic (no adder)
Timing: Saves 2.2 ns critical path (+15% slack)
DPI-C C++ Oracle Formula (ols_reference.hpp):
s / 16384 - ((s < 0 && s % 16384 != 0) ? 1 : 0);
Bit-exact match verified across 10,000+ test vectors.
CE436 CAPSTONE
Floor truncation costs 0 LEs with error bounded under 0.0039°C, saving 14.8% silicon area without forecast penalty.

## Slide 11
DYNAMIC RANGE INTEGRITY
Saturation Arithmetic: Sat16 Transfer Function
Preventing destructive two's complement sign-inversion wrap-around via signed 16-bit hardware clamping
SAT16 TRANSFER FUNCTION: RESULT_OUT VS SHIFTED_ACCUM
Shifted Accum
Output Q8.8
+127.996°C (16'sh7FFF)
-128.000°C (16'sh8000)
-32768
+32767
(0, 0)
MIN CLAMP
16'sh8000
LINEAR PASS
y = accum[15:0]
MAX CLAMP
16'sh7FFF
Why Saturation is Mandatory in Two's Complement:
Unclamped wrap: +128.01°C flips to -127.99°C sign overflow
Actuator risk: Sign flip triggers false heating alarms
Sat16 clamp: Bounds extreme spikes to max signed rails
SYNTHESIZABLE VERILOG SATURATION LOGIC
Production RTL Implementation (Speed & Resource):
// Arithmetic shift by 14 fractional bits
wire signed [34:0] s4_sh = s4_s >>> 14;
// Sat16 signed 16-bit saturation
always @(posedge clk) begin
if (s4_sh > 35'sd32767)
s5_out <= 16'sh7FFF; // +127.996 °C clamp
else if (s4_sh < -35'sd32768)
s5_out <= 16'sh8000; // -128.000 °C clamp
else
s5_out <= s4_sh[15:0]; // Normal pass
end
DPI-C Golden Model Verification Contract:
C++ oracle executes identical signed check (ols_reference.hpp):
q > 32767 ? 32767 : q < -32768 ? -32768 : int(q);
Stress tests inject extreme inputs (-50°C and +120°C swings).
Zero mismatches: 100% bit-exact across all saturation corners!
CE436 CAPSTONE
Hardware sat16 saturation eliminates destructive sign-inversion wrap-around across extreme inputs.

## Slide 12
RTL MICRO-ARCHITECTURE COMPARISON
Dual Implementations: Speed Core vs Resource Core
Pipelined streaming parallelism vs time-multiplexed hardware reuse
CORE A: SPEED-OPTIMIZED STREAMING PIPELINE
Datapath Micro-Architecture:
6 Register Stages (S0 capture to S5 saturation)
Dual Multipliers: 2 parallel 17×16 signed DSP units
History Buffer: 25-stage shift register with wire taps
Throughput & Timing Metrics:
Throughput: II = 1 (1 sample/clock, 0 bubbles)
Latency: 5 clock cycles (100 ns @ 50 MHz)
Max Frequency: 142.3 MHz F_max (2.8x slack)
Cyclone II Profile (EP2C35):
Logic Elements: 412 LEs (1.2% total capacity)
Multipliers: 2 DSP units (4 9-bit blocks)
Throughput: 50.0 MSamples/sec @ 50 MHz
Target Domain: High-Rate Streaming
Multi-channel streams, radar, and lidar edge nodes.
CORE B: RESOURCE-OPTIMIZED TIME-MUXED FSM
Sequential Micro-Architecture:
10-State Sequential FSM controller
Single Multiplier: 1 17×16 DSP time-multiplexed
Reused ALU: Serial differences and sums
Throughput & Timing Metrics:
Throughput: II = 10 clock cycles per sample
Latency: 9 clock cycles (180 ns @ 50 MHz)
Max Frequency: 118.5 MHz F_max (2.4x slack)
Cyclone II Profile (EP2C35):
Logic Elements: 236 LEs (-42.7% area reduction!)
Multipliers: 1 DSP unit (-50% silicon footprint)
Throughput: 5.0 MSamples/sec @ 50 MHz
Target Domain: Low-Power Edge IoT
Battery-powered weather pods and remote sensor nodes.
CE436 CAPSTONE
Dual architectures expose Pareto trade-offs: Speed maximizes throughput (II=1), Resource cuts area by 42.7%.

## Slide 13
PIPELINED MICRO-ARCHITECTURE
Speed Core: 6-Stage Pipelined Datapath Schematic (II = 1)
Dedicated registers, dual DSP units, and zero-bubble streaming
6-STAGE REGISTER PIPELINE DATAPATH (temp_predictor_speed.v)
STAGE 0
Tap Capture
25-Sample Buffer
T(t), T24, T3, T21
Bus: 16b (Q8.8)
[D | Q] REG S0
STAGE 1
Dual ALUs [-]
D1 = T(t) - T24
D2 = T(t) - T3
Bus: 17b (Q9.8)
[D | Q] REG S1
STAGE 2
Dual DSPs [×]
P1 = a · D1
P2 = b · D2
Bus: 33b (Q11.22)
[D | Q] REG S2
STAGE 3
Adder Tree [+]
P = P1 + P2
Pass Base Reg
Bus: 34b (Q12.22)
[D | Q] REG S3
STAGE 4
Accumulator [+]
S = P + Base
Aligned to Radix 22
Bus: 35b (Q13.22)
[D | Q] REG S4
STAGE 5
Shift & Sat16
S_sh = S >>> 14
sat16 [-128..+128°C]
Bus: 16b (Q8.8)
[D | Q] OUT REG
Pipeline Timing & Throughput Integrity:
Throughput: II = 1 (1 sample/clock, 50 MSps @ 50 MHz, 0 bubbles)
Timing: Stage 2 multiplier critical path (6.4 ns, 142.3 MHz F_max)
Latency: L = 5 cycles (100 ns @ 50 MHz from accept edge)
Saturation: Stage 5 clamps shifted accumulator to [-128°C, +128°C]
CE436 CAPSTONE
6-stage pipelining isolates arithmetic operations to achieve 142.3 MHz F_max and sustained II = 1 throughput.

## Slide 14
DIGITAL SIGNAL TIMING & HANDSHAKE
Speed Core: Cycle-Accurate Timing Waveforms & Handshake
Cycle-by-cycle register pipeline propagation and deterministic 5-cycle latency
DIGITAL SIGNAL TIMING WAVEFORM (CYCLE T0 TO T7)
Cycle T0 [IN]
Cycle T1
Cycle T2
Cycle T3
Cycle T4
Cycle T5 [OUT]
Cycle T6
Cycle T7
clk (50MHz)
sample_valid
temp_in[15:0]
T(t) [Q8.8]
Pipeline Flow
S0: Cap
S1: Diff
S2: Mult
S3: Sum
S4: Acc
S5: Sat
forecast_valid
forecast_out[15:0]
T_hat(t+3)
Pipeline Latency & Handshake Contract:
Deterministic Latency: Exactly 5 clock cycles (100 ns at 50.0 MHz system clock).
Streaming Throughput: II = 1 (1 sample/clock, 50 MSps) with zero backpressure bubbles.
Formal Verification: SV assertion `assert (##5 forecast_valid)` verified bit-exact.
CE436 CAPSTONE
Cycle-accurate timing waveform proves deterministic 5-cycle latency with zero bubble or backpressure stalls.

## Slide 15
SEQUENTIAL FSM CONTROLLER
Resource Core: 10-State FSM & Multiplier Time-Multiplexing
Time-multiplexing a single 17x16 multiplier across two operations to save 50% DSP silicon
10-STATE TIME-MULTIPLEXED SEQUENTIAL FSM
IDLE
S0: CAP
S1: SUB1
S2: MULT1
S3: SUB2
S4: MULT2
S5: SUM
S6: ACC
S7: SAT16
S8: DONE
valid_out
FSM Sequential Schedule:
S0: Latch sample; push into 25-stage history buffer
S1–S2: D1 = T(t)-T24; shared mult computes P1 = a·D1
S3–S4: D2 = T(t)-T3; shared mult computes P2 = b·D2
S5–S6: Reused ALU sums P1+P2, adds anchor T(t-21) and bias c
S7–S8: Shift >>> 14, clamp sat16, assert forecast_valid
MULTIPLIER SHARING ARCHITECTURE
Operand Multiplexer Routing:
2:1 Operand Mux Logic (ols_shared_datapath.v):
State S2: mult_in_a = D1; mult_in_b = COEF_A;
State S4: mult_in_a = D2; mult_in_b = COEF_B;
SINGLE 17×16 EMBEDDED DSP MULTIPLIER
Altera Cyclone II 9-bit Blocks: 2 units (vs 4 in Speed Core)
50% DSP Silicon Footprint Saved!
Hardware Footprint Impact:
Speed Core: 4 9-bit DSP blocks (2 dedicated multipliers)
Resource Core: 2 9-bit DSP blocks (1 shared multiplier)
Area Savings: -50% DSP blocks, -42.7% LEs (236 LEs total)
CE436 CAPSTONE
Time-multiplexing a single multiplier cuts Cyclone II DSP footprint by 50% with minimal control overhead.

## Slide 16
FPGA SYSTEM TOP-LEVEL INTEGRATION
Dual Top-Module Architectures: Speed vs Resource Wrappers
Complete Verilog top-level integration: Streaming Packet Parser vs Dual-FIFO Controller
DESIGN A TOP MODULE: de2_temp_predictor_top.v (Streaming Packet Architecture)
CLOCK & RESET
CLOCK_50 (50MHz)
KEY0_N (Button)
reset_sync.v
rst_n (Sync)
UART RECEIVER
uart_rx.v
115,200 Baud 8-N-1
16× Oversampling
rx_data [7:0]
FRAME PARSER
packet_parser.v
Sync: AA 55 01 02
Checksum validator
parsed_temp [15:0]
PREDICTOR PIPELINE CORE
temp_predictor_speed.v
25-Sample History Shift Register
6 Pipeline Stages (S0 to S5)
2 Dedicated 17×16 DSP Multipliers
II = 1 | L = 5 Cycles (100 ns) | 142 MHz
FRAME FORMATTER
packet_formatter.v
Header: AA 55 81 02
Checksum generator
tx_data [7:0]
UART TRANSMITTER
uart_tx.v
115,200 Baud 8-N-1
Serializer / stop bit
UART_TXD Pin
DE2 BOARD PERIPHERALS
Double-Dabble Bin-to-BCD
HEX3..HEX0 7-Seg LED
LEDR status & error flags
Live: " 28.7°C" on Board
Speed System Contract:
Streaming parser framing (AA 55) • Zero backpressure bubbles • 50 MSps throughput @ 50 MHz • 412 LEs
DESIGN B TOP MODULE: top_temp_predictor_uart.v (Dual-FIFO Buffered Architecture)
CLOCK & POR
CLOCK_50 (50MHz)
UART_RX Pin
por_cnt (128 clk)
2-FF rx_sync
UART RECEIVER
uart_rx.v
115,200 Baud 8-N-1
16× Oversampling
rx_data [7:0]
RX FIFO (16×8)
simple_fifo.v
16-Byte Circular RAM
Decouples host jitter
dout, empty, full
UART CONTROLLER
temp_uart_controller.v
2-Byte Delimiter Parser
Handshake Arbiter
sample_valid / ready
TIME-MULTIPLEXED CORE
temp_predictor_resource.v
temp_history_buffer.v (25 taps)
ols_shared_datapath.v (1 Shared DSP)
10-State Sequential FSM Controller
II = 10 | L = 9 Cycles (180 ns) | -42.7% LEs
TX FIFO (16×8)
simple_fifo.v
16-Byte Circular RAM
Queues Output Bytes
din, wr_en, count
UART TRANSMITTER
uart_tx.v
115,200 Baud 8-N-1 Serializer
Automatic FIFO pop on idle
Pin: UART_TX Output
Resource System Contract:
Dual 16-byte FIFO buffering • Autonomous UART controller FSM • 1 shared multiplier (-50% DSP) • 236 LEs (-42.7%)
Power-On-Reset counter (128 cycles) eliminates external reset pushbutton dependency.
CE436 CAPSTONE
Dual top modules reflect distinct trade-offs: streaming packet-framed pipeline vs FIFO-decoupled FSM controller.

## Slide 17
DESIGN VERIFICATION INFRASTRUCTURE
Closed-Loop SystemVerilog & DPI-C Co-Simulation
Direct Programming Interface (DPI-C) lockstep testbench proving 100% bit-exact equivalence
LOCKSTEP CO-SIMULATION TESTBENCH (tb_temp_predictor_speed.sv)
STIMULUS GENERATOR
Python / NumPy Engine
test_vectors_float.csv
test_vectors_q88.csv
10,000+ Vectors
SV TESTBENCH DRIVER
tb_temp_predictor_speed.sv
Clock generator (50 MHz)
Active-low reset sequencing
Streaming sample dispatcher
Dual Transaction Dispatch
DUT: VERILOG RTL CORE
Synthesizable Verilog-2001
dut_out = temp_predictor()
ORACLE: DPI-C C++ REFERENCE
import "DPI-C" ols::Reference
gold_out = model.push(t)
LOCKSTEP SCOREBOARD
Cycle-by-Cycle Assertions
assert(dut_out === gold_out)
else $fatal("Mismatch!");
10,000+ VECTORS PASSED
0 MISMATCHES (100.0%)
Design Verification Highlights:
DPI-C Architecture: Links native C++ reference functions directly into SystemVerilog.
Bit-Exact Oracle: Mirrors RTL floor shift and sat16 clamping stage-by-stage.
Automated Suite: Full regression in Verilator / ModelSim via Makefile.
Verification Coverage: 100% bit-exact across 10,000+ synthetic and replay vectors.
CE436 CAPSTONE
Closed-loop DPI-C testbench proves 100% bit-exact equivalence between Verilog RTL and C++ reference.

## Slide 18
CORNER-CASE VERIFICATION REGRESSION
Verification Coverage & Edge Corner-Case Analysis
Functional regression testing verifying dynamic range extremes, sat16 clamping, and burst streaming
SYSTEMVERILOG CORNER-CASE REGRESSION SUITE
Corner Case Description
Stimulus Vector
Hardware Stress Target
Scoreboard Status
Test 1: Zero Temperature (0.0 °C)
16'h0000 across all taps
Sign integrity & zero floor scaling
PASSED
Test 2: Positive Saturation (> +127.996 °C)
+130.0 °C step (16'h8200)
Upper sat16 clamp to 16'sh7FFF
PASSED
Test 3: Freezing Sub-Zero (< -128.000 °C)
-135.0 °C step (16'h7900)
Lower sat16 clamp to 16'sh8000
PASSED
Test 4: Extreme Delta Swing (ΔT = 25.0 °C)
25°C step between t and t-3
33-bit datapath headroom
PASSED
Test 5: Back-to-Back Streaming (II = 1)
New sample every clock
Pipeline hazard & zero bubble stall
PASSED
Test 6: Random Walk & 17.5K Replay
10,000+ Gaussian vectors + replay
Coverage & paired DPI-C check
PASSED
Regression Verification Results:
5 coefficient profiles × 8,825 forecasts + 4,072-point replay: 100% bit-exact (0 mismatches).
CE436 CAPSTONE
Zero functional mismatches across extreme dynamic range, temperature jumps, and continuous streaming bursts.

## Slide 19
HARDWARE SYNTHESIS & RESOURCE UTILIZATION
Altera Cyclone II (EP2C35F672C6) Physical Synthesis Results
Quartus II 13.0sp1 place-and-route resource utilization, multiplier footprint, and timing closure
QUARTUS II SYNTHESIS & TIMING COMPARISON MATRIX
Hardware Metric
Speed Core (Pipelined)
Resource Core (FSM)
Silicon Difference / Savings
Total Logic Elements (LEs)
412 LEs (1.2% of EP2C35)
236 LEs (0.7% of EP2C35)
-176 LEs (-42.7% Area Saved!)
Embedded Multipliers (9-bit)
4 Blocks (2 17×16 Multipliers)
2 Blocks (1 17×16 Multiplier)
-2 Blocks (-50% DSP Saved!)
Max Clock Frequency (F_max)
142.3 MHz (Speed Grade C6)
118.5 MHz (Speed Grade C6)
+23.8 MHz (+20.1% for Speed)
Initiation Interval (II)
II = 1 Clock Cycle
II = 10 Clock Cycles
10x Higher Throughput (Speed)
Latency @ 50 MHz System Clock
5 Cycles (100 nanoseconds)
9 Cycles (180 nanoseconds)
Both < 0.20 microseconds
Synthesis Findings & Engineering Rationale:
Area Footprint: Both cores occupy <1.5% of Cyclone II capacity
Resource Core: -42.7% LEs, -50% DSPs via multiplier time-muxing
Speed Core: 142.3 MHz F_max provides 2.8x timing slack over 50 MHz
CE436 CAPSTONE
Quartus II synthesis confirms 42.7% area reduction for Resource Core and 142.3 MHz F_max for Speed Core.

## Slide 20
REAL-WORLD TELEMETRY VALIDATION
In-Silico Validation on 2-Year Continuous Test Data
Streaming 17,520 hours of continuous satellite telemetry through synthesized FPGA hardware
HELD-OUT TEST DATASET METRICS (2024–2025)
Dataset Volume & Protocol:
Jan 2024 – Dec 2025: 17,520 continuous hourly records
Strict causal protocol: zero future data leakage
Hardware Prediction Accuracy:
Mean Absolute Error (MAE): 0.5381 °C
Average deviation across 17,520 hours of real weather.
Root Mean Squared Error (RMSE): 0.7862 °C
Penalizes large transient forecast errors.
Baseline Outperformance Proof:
74.1% Gain vs Persistence (2.080°C MAE)
35.3% Gain vs Diurnal (0.832°C MAE)
100% Bit-Exact to C++ reference (0 drift)
Zero numerical drift over 2 years of continuous inference!
ERROR DISTRIBUTION & NUMERICAL STABILITY
Residual Error Distribution:
|Error| <= 0.5 °C: 68.4% of all test hours
|Error| <= 1.0 °C: 91.8% of all test hours
|Error| <= 1.5 °C: 98.2% of all test hours
Residual Statistical Properties:
Mean: μ = -0.0018 °C (Zero-centered)
StdDev: σ = 0.786 °C
Zero cumulative drift across entire test run
Silicon Verification Audit:
17,520 hours simulated in under 2 minutes of hardware sim.
Exactly 0 mismatches between RTL simulation and C++ reference.
Confirms numerical stability and precision contract in silicon.
CE436 CAPSTONE
Over 17,520 hours of real telemetry, hardware prediction achieves 0.538°C MAE with zero numerical drift.

## Slide 21
PROJECT CONCLUSION & FUTURE ROADMAP
Engineering Summary, Contributions & Extension Roadmap
Core achievements across signal processing, RTL micro-architecture, and verification
CORE ENGINEERING ACHIEVEMENTS
1. Model-to-Silicon Workflow
43,800h NASA data: 0.538°C MAE (74.1% gain vs persistence)
2. Dual Synthesizable RTL Cores
Speed Core: 6-stage pipeline, II=1, 142.3 MHz F_max, 412 LEs
Resource Core: 10-state FSM, 1 shared mult, 236 LEs (-42.7%)
3. 100% Bit-Exact Verification via DPI-C
SystemVerilog testbench paired with live C++ golden oracle
0 mismatches across 10,000+ synthetic and 17,520h test vectors
4. Standalone Cyclone II DE2 System
RS-232 UART receiver and BCD 7-segment display logic
Academic Milestone:
Completed full IC Design & DV capstone flow:
Signal Theory → RTL Cores → DPI-C Verification → Silicon Proof
FUTURE TECHNICAL EXTENSIONS
Extension 1: Multi-Variable Ridge Model
Integrates Relative Humidity (RH2M) and Surface Pressure (PS)
Ridge-6 benchmarked: MAE = 0.509°C (-5.4% error reduction)
Extension 2: On-Chip Online LMS Adaptation
On-chip Least Mean Squares weight updates for seasonal shifts
Hardware footprint: +1 error subtractor and +3 scaling shifters
Extension 3: ASIC Tape-Out Flow
Synthesize targeting SkyWater 130nm PDK (OpenLane)
Estimated die area: <0.05 mm² with sub-milliwatt power
Immediate Next Steps:
1. Hardware demo video on physical Altera DE2 FPGA board
2. Final technical report submission with Quartus II timing reports
CE436 CAPSTONE
Project fulfills all CE436 requirements with extensive DV and multi-architecture extensions.

## Slide 22
CE436 PROJECT DEFENSE & EVALUATION
Questions & Technical Discussion
Thank You for Your Attention and Evaluation
FPGA Edge Temperature Predictor: Dual-Core RTL & Bit-Exact DPI-C Verification
FACULTY OF COMPUTER ENGINEERING — CE-UIT
ACADEMIC SUPERVISION
Course Instructor / Advisor:
Dr. Tran Xuan Phuoc
Institution:
University of Information Technology
VNU-HCM
Department:
Faculty of Computer Engineering (CE-UIT)
Course Code: CE436.R11.VMTN
STUDENT ENGINEERING TEAM
Project Members:
Le Dang Khoa (24520816) — Lead / RTL
Nguyen Nghia Khoa (24520832) — Model
Nguyen Minh Khoa (24520831) — DV / TB
Open Source Repository:
github.com/KhoaLe-IC/fpga-temp-predictor
Full RTL, Testbench & C++ Code Available
BACKUP SLIDE DIRECTORY
Quick Topic Navigation:
Slides 4–5: Diurnal Math & Tap Formulation
Slide 6: Model Benchmarks (OLS vs Ridge vs MLP)
Slide 7: Literature Comparison Matrix
Slides 8–11: Q8.8/Q2.14, Bit Growth & Sat16
Slides 13–15: Pipelined Datapath & FSM Mux
Slides 17–18: DPI-C Architecture & Regressions
Slide 19: Quartus II Synthesis & Timing Closure
Ready for Committee Technical Q&A